## Slide 1
ATRIUM
Open SDN Distribution
Saurav Das
Principal System Architect, ONF
With contributions from ONF Atrium Management team and many others …

## Slide 2: Outline
Project Atrium today
  Motivation
  Atrium release 15/A
Project Atrium next
  What is coming in the next release 15/B?
Project Atrium roadmap
  - Tentative: projects under discussion
https://groups.opensourcesdn.org/wg/Atrium/dashboard
LEARN MORE & JOIN THE COMMUNITY:

## Slide 3
SDN Provides a Lot of Choices

## Slide 4
Solution: Vertically Integrated Stack
== SDN Distribution

## Slide 5
Project Atrium Goals
Integration
  Create vertically-integrated open-source stacks
  From open-source components, OF1.3 & Hardware
  Enable network operators to download distribution
  from a single location
Interoperability
  Enable multiple hardware vendors to plugin to stack
  Allows end-users to select different hardware classes
  for common use-cases.
Deployments
  Work hand-in-hand with operators on deployable use
  cases leading to trials.
  - Give operators confidence in pure SDN solutions

## Slide 6
ONOS
What is Atrium today?
vlan x
vlan y
vlan z
E-BGP
E-BGP
BRCM ASIC
OF-DPA
Indigo OF Agent
OF-DPA API
OpenFlow 1.3
OCP
Software
-
ONL
ONIE
OCP Bare Metal Hardware
BRCM SDK API
OCP: Open Compute Project; ONL: Open Network Linux; ONIE: Open Network Install Env;
BRCM: Broadcom Merchant Silicon ASICs; OF-DPA: OpenFlow Datapath Abstraction
OFDPA Driver
Peering Application
Quagga BGP

## Slide 7
ONOS
What is Atrium today?
vlan x
vlan y
vlan z
E-BGP
E-BGP
Vendor Hardware
OpenFlow 1.3
OF Agent
OFDPA Driver
Peering Application
Quagga BGP

## Slide 8
ONF Builds 7 Routers

## Slide 9
A Closer Look at Interoperability
Accton, Quanta (BRCM ASIC)
NoviFlow, Netronome
(NPU/NFP)
Corsa
(FPGA)
Pica8
(BRCM ASIC)
Centec
(ASIC)
Different combinations of
Match-Action Tables form
Different OF 1.3 pipelines
How can a controller manage these differences?
How can an application work across these differences?

## Slide 10
SDN Application
Flow Objectives
OFDPA Driver
Controller
Switch
OpenFlow 1.3
OpenFlow 1.3
Write the app once
without pipeline details
adapt to specific
Pipeline using
device driver
Accton, Quanta (BRCM ASIC)
NoviFlow, Netronome
(NPU/NFP)
Corsa
(FPGA)
Pica8
(BRCM ASIC)
Centec
(ASIC)
SoftRouter Driver
Corsa Driver
Pica8
Driver
Centec Driver
Solution: Flow Objectives API

## Slide 11: Example: Filtering Objective
Filter  only Permit or Deny options
On match fields of packet header
Router port: X
Permit: MAC 1, VLAN 1, IP 1, 2, 3
Permit: MAC 1, VLAN 2, IP 4, 5
Corsa Driver
OF-DPA Driver
T0
mac
T2
port-vlan
T4/5
T6
ip
T0
port
T1
Port-vlan
T2
mac
T4
ip
Flow Objectives

## Slide 12: Example: Next Objective
Next  next hop for forwarding
Similar to OF 1.3 group, but …
NEXT- HOP
Corsa Driver
bkt
Indirect group
NoviFlow & Pica8 Drivers
 Flow-actions
bkt
OF-DPA Driver
Group chain
Flow Objectives

## Slide 13: Atrium Demo @ SDN Solution Showcase
V1
Hosts (1.0.0.1)
Hosts (2.0.0.1)
NoviFlow
Accton
Netronome
Q1
Corsa
Quanta
Q2
V2
Pica8
Centec
bgp1> sh ip bgp summary
BGP router identifier 192.168.10.101, local AS number 65000
RIB entries 3, using 336 bytes of memory
Peers 5, using 22 KiB of memory
Neighbor V AS MsgRcvd MsgSent TblVer InQ OutQ Up/Down State/PfxRcd
1.1.1.1 4 65000 30090 31109 0 0 0 1d01h43m 0
192.168.10.1 4 65001 31095 31114 0 0 0 1d01h43m 1
192.168.11.1 4 65101 30775 30784 0 0 0 21:07:07 1
192.168.13.1 4 65301 28322 28339 0 0 0 18:11:55 1
192.168.22.1 4 65201 25959 25974 0 0 0 21:23:24 1
Total number of neighbors 5
bgp1> sh ip bgp
BGP table version is 0, local router ID is 192.168.10.101
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal,
r RIB-failure, S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
*> 1.0.0.0/24 192.168.10.1 1 0 65001 i
* 2.0.0.0/24 192.168.22.1 0 65201 65202 65203 65002 i
* 192.168.13.1 0 65301 65302 65303 65002 i
*> 192.168.11.1 0 65101 65102 65002 i
Total number of prefixes 2
AS65301
AS65302
AS65201
AS65202
AS65203
AS65000
AS65303
AS65002
AS65102
AS65101
AS65001

## Slide 14: Atrium Pre-release Deployment

## Slide 15: Atrium Post-release Operator Engagements

## Slide 16: Atrium Post-release Operator Engagements

## Slide 17: Outline
Project Atrium today
  Motivation
  Atrium release 15/A
Project Atrium next
  What is coming in the next release 15/B?
Project Atrium roadmap
  - Tentative: projects under discussion
https://groups.opensourcesdn.org/wg/Atrium/dashboard
LEARN MORE & JOIN THE COMMUNITY:

## Slide 18: What’s Coming in the 15/B Release?
Continued Improvements on the 15/A release (ONOS based)
  Hardening & Stability
  Performance
  Missing features: untagged, runtime-config, static-routes
  Hardware Automated Test Infrastructure
2. Atrium Router on OpenDaylight
- Porting from ONOS to ODL
- ODL will also use FlowObjectives and device drivers
- Community contibutions: Wipro & Criterion
https://groups.opensourcesdn.org/wg/Atrium/dashboard
LEARN MORE & JOIN THE COMMUNITY:

## Slide 19
Open-Source Leaf-Spine Fabric (L3 Clos)
Internally the Fabric uses MPLS Segment Routing

## Slide 20
Open-Source Leaf-Spine Fabric (L3 Clos)
Internally the Fabric uses MPLS Segment Routing

## Slide 21: Outline
Project Atrium today
  Motivation
  Atrium release 15/A
Project Atrium next
  What is coming in the next release 15/B?
Project Atrium roadmap
  - Tentative: projects under discussion
https://groups.opensourcesdn.org/wg/Atrium/dashboard
LEARN MORE & JOIN THE COMMUNITY:

## Slide 22
L2 IXP Fabric
Route Server
1 MAC per port,
1 MAC per VLAN per port
No broadcast, multicast, STP, OSPF, etc.

## Slide 23
Atrium Router Stack
+
L3 Clos Fabric
=
Chassis Routers
SDN Controller
BGP
App

## Slide 24
Support MEF E-Line Services
Cust. A
Cust. B
Cust.
A
Cust. B
EPL/ EVPL
Segment-Routed
Pseudowires

## Slide 25
This is just the starting point!
ONOS
BGP
IGP
ONOS
BGP
IGP
ONOS
BGP
IGP
Global Controller
TE

## Slide 26: And more …
Generic L2 Enterprise Network
Smart Cities/ IoT
Packet-Optical

## Slide 27
Summary
Integration, Interoperability & Deployments
  Atrium 1st release brings together ONOS, Quagga, OCP components (ONL, ONIE) and OFDPA with white-boxes + vendor equipment
  Open SDN Distribution (2015/A release: June 30th)
  ONF builds 7 routers!
  Key architectural contribution: Flow Objectives & Device Drivers
  Pre release deployment in Sydney.
  More coming as we engage operators
Atrium 15/B release
  Improved 15/A router built around ONOS
  ODL based Atrium router
  Atrium leaf-spine L3 Clos fabric
Many more projects in the horizon

## Slide 28: ONOS Architecture
OpenFlow Provider (1.0, 13)
Netconf Provider
PCEP
Provider
TL-1
Providers
Providers
Core Services (distributed)
Applications
(distributed)
Host Provider
LLDP Provider
Topology Service
Link Service
Device Service
Host Service
Intent
Service
Stats Service
Flow Rule Service
Group
Service
Packet Service
Segment Routing
SDN-IP
BGP Router
Flow Objectives
Driver X
Driver Y
Driver Z
Optical
Mastership Service
I-BGP Speaker/RIB
I-BGP Speaker/RIB