## Slide 1: CORD: Transforming Service Provider Access Infrastructure Saurav Das Principal Architect, ONF

## Slide 2
Why CORD?
CORD Technology Differentiators
Different Flavors of CORD
Outline
Outline

## Slide 3
G/GE/XG-PON
xDSL/G.Fast
Cable/Docsis
Access
Switch
Ethernet
Aggregation Switch
BNG (router with per subscriber policies)
Residential
Subscribers
TV
Internet
Landlines
Home Sec etc.
Enterprise
Customers
Ckts: T1/E1/DS3
Carrier Ethernet
MPLS VPNs
Carrier Ethernet
Switch
PE- Router
Optical Transport Switch
MME/HSS
S-GW
P-GW
Firewall
DPI
CDN
Message
Router
Carrier Grade NAT
Session Border
Controller
Carrier Grade NAT
DPI
DPI
SP Access Network Evolution
Mobile (Cellular)
Subscribers
Voice
Data
Video
Access is a large part of SP Business
Backhaul
Switch
WAN
Accelerator
IDS/IPS
Firewall
Notes: Let’s start with a thought experiment – lets say I was a large service provider, and I had a residential, enterprise and cellular subscriber base.
The first thing to recognize is that Access solutions are a massive part of the SP business. Yes metro and long-haul core networks are nice, but they are shared (amortized) by the usage of millions of subscribers. The real costs are in reaching those millions of customers.
So lets say I needed to build the infrastructure for this customer base to provide the services each set needs. . I might say that …

## Slide 4
G/GE/XG-PON
xDSL/G.Fast
Cable/Docsis
Access
Device
Ethernet
Aggregation
Switch
BNG (router with per subscriber policies)
Residential
Subscribers
Enterprise
Customers
Carrier Ethernet
Switch
PE- Router
Optical Transport Switch
MME/HSS
S-GW
P-GW
Firewall
DPI
CDN
Message
Router
Carrier Grade NAT
Session Border
Controller
Firewall
Firewall
Carrier Grade NAT
Carrier Grade NAT
DPI
DPI
Mobile (Cellular)
Subscribers
Access is a large part of SP Business
Backhaul
Device
WAN
Accelerator
By some counts  50-300 different boxes in a large CO
Tremendous source of high Capex/Opex
Not agile  hard to manage/operate  hard to create new services
Is there a transformative approach?
SP Access Network Evolution
Notes: At&T alone operates thousands of these each serving 10 – 100k subs
By one count more than 300 different boxes in a large CO

## Slide 5
Residential
Subscribers
Enterprise
Customers
Mobile (Cellular)
Subscribers
Access is a large part of SP Business
Thought Experiment
Access Adaptation Layer
WAN Adaptation Layer
Service Creation Platfrom
-- Onboarding, Composition, Orchestration, Analytics
Control Plane Services
-- Authentication
-- Per subscriber policies
-- Plumbing control
Data Plane Plumbing
-- Switching, Routing
-- Virtualization, Encaps
-- Service Chains
Data Plane Services
-- Spl. Fn: DPI, NAT, IDS
-- Policy Enforcement: FW
-- Opt.: CDN, WanX
WAN
Protocols,
Encaps,
Optical
Services APIs for Operators & Customers
Notes: Instead of thinking about boxes that do many functions, or boxes that do the same thing as other boxes but with a different name for a different market, lets think in terms of building blocks.
We can readily recognize from the previous slide that there are common elements in each set of services and infrastructures. So it really makes sense to think in terms of building blocks
For each of these building blocks, why stay stuck in 50 years of legacy. Why not use the best of breed technology that has emerged over the last 10 years.

## Slide 6
ONOS Controller Cluster
vRouter
Control
vOLT Control
Virtual Network
Overlay
Fabric
Underlay
Other Apps
(Aux/Policies)
XOS
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
vSG
vSG
vSG
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
vSw
vSw
vSw
vSw
vSw
R,
E,
M
Access
Thought Experiment CORD
Access Adaptation Layer
WAN Adaptation Layer
Service Creation Platfrom
-- Onboarding, Composition,
Orchestration, Analytics
Services APIs for Operators & Customers
Control Plane Services
-- Authentication
-- Per subscriber policies
-- Plumbing control
Data Plane Plumbing
-- Switching, Routing
-- Virtualization, Encaps
-- Service Chains
Data Plane Services
-- Spl. Fn: DPI, NAT, IDS
-- Policy Enforcement: FW
-- Opt.: CDN, WanX
Notes: Instead of thinking about boxes that do many functions, or boxes that do the same thing as other boxes but with a different name for a different market, lets think in terms of building blocks.
We can readily recognize from the previous slide that there are common elements in each set of services and infrastructures. So it really makes sense to think in terms of building blocks
For each of these building blocks, why stay stuck in 50 years of legacy. Why not use the best of breed technology that has emerged over the last 10 years.

## Slide 7
Central Office
Proprietary Access Devices & Archaic Operations at the Network Edge
Data Center
Commodity Hardware & Agile Software
Values Edge Presence
Values Commodity & Agility
Today
IoT, self-driving cars, VR/AR, AI, NLP, 4kTV, connected-cars, smart-cities
Low latency, edge computing, different traffic flows
Next Gen
Services:
Next Gen
Platform:
Service Providers not threatened by
Google, Amazon, MSFT, FB’s use of
Commodity hardware! Real pressure is from OTT Services
Notes: AT&T is not threatened not just by Google's commodity hardware, per se (of course they'd like to replicate it so they too can enjoy reduced costs),
AT&T isn't going to increase revenue just by re-creating their current suite of services on commodity.

## Slide 8
Tomorrow
CORD
Economies and Agility of the Datacenter &
Low Latency and Computing at the Edge
  For SP’s to provide new services
  For SP’s to provide access to third-party services
CO
DC
Central Office Re-architected as a Datacenter
Notes: that once we'd gained parity with the status quo, the real value was in what we would enable next.
But we must look beyond Capex/Opex savings as the only benefit of CORD, because that is only half of the story.
The other half is the fact that with CORD, we are bringing the ability to take advantage of low-latency and edge-computing to the access.
We know that nearly all future services will benefit from these features, but it will require flexible cloud-like infrastructure at the access, not far-away in some DC.

## Slide 9
CORD’s Unifying Principle
SDN
Programmability & White-Boxes
NFV
VNFs & Disaggregation
Cloud
Agility & Microservices
XaaS
Common platform
all markets
all services
Commodity hardware
Open-source software
- building blocks
Everything as a Service
- XaaS
Economies and Agility of the Datacenter &
Low Latency and Computing at the Edge
  For SP’s to provide new services
  For SP’s to provide access to third-party services
Notes: We use the best of breed technology that has emerged over the last 10 years to create one common platform

## Slide 10: Operator Plans
Tremendous interest from SP’s all over the world
  AT&T
  Comcast
  Google
  Verizon
  Windstream
  Bell Canada
Deutsche Telecom
Telefonica
Telecom Italia
Orange
Vodafone
British Telecom
NTT
China Mobile
China Unicom
SK Telecom
KDDI
Telstra
North America
EMEA
Asia Pacific
Independent Survey Results: 20 operators (control 33% of world’s telecom Capex)
  30% plan to deploy CORD by end of 2017
  40% plan to deploy CORD beyond 2017
  15% don’t know yet, 15% have no plans
Michael Howard, Infonetics Research (IHS)
https://www.sdxcentral.com/articles/news/ihs-markit-70-carriers-will-deploy-cord-central-office/2017/01/

## Slide 11
Why CORD?
CORD Technology Differentiators
Different Flavors of CORD
Outline
Outline

## Slide 12: [1] Disaggregation
SDN
NFV
Cloud
Residence
Central Office
CPE
ONU
OLT
Backbone
Network
vSG
vOLT
vRouter
Leaf-Spine Fabric
BNG
ETH AGG
Residence
Central Office
CPE
ONU
OLT
ETH AGG
BNG
Backbone
Network

## Slide 13: NFV Today
pX
pY
pZ
vX
vY
vZ
Make virtual (software) versions of hardware eqiupment/appliances
Chain them together
Worry about performance (DPDK, VPP etc.) …

## Slide 14: [2] CORD Service Composition
SDN
NFV
Cloud
pX
pY
pZ
pX
pY
pZ
1. Disaggregate
Monolithic Hw
2. Scale each function/
microservice
independently
3. Compose end-user
services
CORD composes scalable services, instead of simply chaining VMs

## Slide 15: [2] CORD Service Composition
SDN
NFV
Cloud
Controller
vSG
Controller
vRouter
Residential
Subscribers
vOLT
Controller
Controller
vCDN
vG.Fast
Controller
v10GPON
Controller
Enterprise
Customers
Controller
vCPE
Mobile
Subscribers
vBBU
Controller
Controller
vSGW
Controller
vCE
…

## Slide 16: [3] SDN Controlled P + V Infrastructure
SDN
NFV
Cloud
1. DC Leaf-Spine Fabric Underlay
2. Virtual Network Overlay
3. Unified SDN Control
over underlay & overlay
ONOS
Controller Cluster & Apps
Unique combination of these three components
Common control provides opportunites for optimized service delivery
Example: Many operators have told us CORD vRouter is best-of-breed

## Slide 17
vRouter as a VNF?
Dataplane
Control Plane
(OSPF, BGP ..)
Management (CLI, SNMP, NetCONF)
Control Plane
(OSPF, BGP ..)
Dataplane
Management (CLI, SNMP, NetCONF)
VNF = vRouter VM
(vCPE, vBNG,
vPGW, vBRAS)
CP
DP
vRouter
VM
Underlay Network
VNF
VNF
VNF
Issues: Hairpinning
Embedded control plane complicates scale-out
VNFM
(VNF Manager)
DP
DP
DP
DP
DP
CP
Issue: Still hairpinning through a load-balancer
vRouter as VNF?

## Slide 18
ONOS Controller Cluster
ONOS Controller Cluster
OLT
OLT
OLT
To residential
subscribers
VM
VM
Trellis vRouter
Underlay Control
OSPF
I-BGP
vRouter
Quagga
(or other)
Router
Router
To Upstream
(Metro) Network
ONOS
XOS
Overlay Control
OVS
OVS
VNF
VNF
OVS
OVS
CORD vRouter Operation

## Slide 19
ONOS Controller Cluster
ONOS Controller Cluster
OLT
OLT
OLT
To residential
subscribers
VM
VM
Trellis vRouter
Underlay Control
OSPF
I-BGP
vRouter
Quagga
(or other)
Router
Router
To Upstream
(Metro) Network
ONOS
XOS
Overlay Control
OVS
OVS
VNF
VNF
OVS
OVS
CORD vRouter Operation

## Slide 20
ONOS Controller Cluster
ONOS Controller Cluster
OLT
OLT
OLT
To residential
subscribers
VM
VM
Trellis vRouter
Underlay Control
OSPF
I-BGP
vRouter
Quagga
(or other)
Router
Router
To Upstream
(Metro) Network
ONOS
XOS
Overlay Control
OVS
OVS
VNF
VNF
OVS
OVS
CORD vRouter Operation

## Slide 21
ONOS Controller Cluster
ONOS Controller Cluster
ONOS
OLT
OLT
OLT
To residential
subscribers
vSG
vSG
Optimized Multicast in R-CORD
Underlay Control
Multicast Control
IGMP
Snooping
PIM-SSM
Router
Router
To Upstream
(Metro) Network
XOS
CORD vRouter Operation - multicast

## Slide 22
Why CORD?
CORD Technology Differentiators
Different Flavors of CORD
Outline
Outline

## Slide 23
BRCM Tomahawk / Cavium/Barefoot
32 or 64 X 100G
BRCM Tomahawk / Cavium/Barefoot
32 or 64 X 100G
Remote CO
BGP
Upstream Dataplane Integration
Micro-OLT
Multi-vendor
ONT/ONU
Qumran MX
XOS
ONOS
ONOS
Upstream Orchestrator Integration
VOLTHA
VOLTHA
VOLTHA
VNF
VNF
VNF
BNG (QoS)
Maple
Qumran AX
Maple
Qumran AX
Other Vendor OLT
Other Vendor OLT
100G
100G
100G
100G
1-2 racks of Edge compute
B
B
ONOS
VOLTHA
VNF
XGS-PON, G/GE-PON, G.Fast, micro-OLT
Fast path design (Internet connectivity)
BNG in leaf-switches (Qumran)
100G spine/aggregation switches
Upsteam integration (orchestration)
10G
R-CORD

## Slide 24: M-CORD (last year)
Leaf-Spine
Fabric
ONOS + XOS + OpenStack/Docker
Disaggregated/Virtualized RAN & EPC,
Mobile Edge Applications,
Network Slicing
vBBU
RRUs
vMME
vSGW
vPGW-D
vPGW-C
Content
Caching
Disaggregated(Split)/ Virtualized RAN
Disaggregated/ Virtualized EPC
Mobile Edge
Applications

## Slide 25
Disaggregation of MME & Connectionless GW for Static IoT Devices
  Utilizing open source EPC & RAN stacks (except layer 1) from multiple vendors
MWC`17 DEMO
DEMO 2
Static IoT devices are served by disaggregated MME (w/o mobility management) and GTP-less S/PGW to achieve control signal reduction
Connectionless GW
Disaggregated MME
CP Signal for Regular LTE device
UP Traffic for Regular LTE device
CP Signal for Static IoT device
UP Traffic for Static IoT device
Static IoT devices
Core Slice for
IoT devices
Core Slice for
Regular LTE handsets

## Slide 26: E-CORD
Observe, Control, Adapt
Value-added
Services
Security, policy control, …
Virtual Network as a Service
Integrated Analytics
SD-WAN, Simple on-prem
SDN Control Plane ONOS
NFV Orchestration XOS
SDN Fabric
Commodity servers, switches, network access
+
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
Carrier-grade Network as a Service
Built on an open platform Bring data center economy and cloud agility
Carrier Ethernet
L3VPN
SD-WAN application policies
Any VNF Firewall, WAN-X, encryption, …
Any location On prem, CO, cloud
Active probes
Programmable probes

## Slide 27
Why CORD?
  Economies & Agility of a DC
  Low latency & Edge-compute at a CO
  CORD = SDN + NFV + Cloud
CORD Technology Differentiators
  Disaggregation
  Service composition, not just service chaining
  Unified SDN control of Physical & Virtual networking
Different Flavors of CORD
  R-CORD: XGS-PON, BNG in white-box hardware
  M-CORD: 5G exploration & enablement (slicing/connectionless/X-RAN)
  E-CORD: SD-WAN for SPs
Outline
Summary
opencord.org