## Slide 1
High Availability
In Disaggregated Networks
Saurav Das
Principal Architect, ONF
With contributions from many others …

## Slide 2
Outline
Example Disaggregated Network
High Availability in Disaggregated Networks
Open-source, SDN-based
Datacenter Leaf-Spine Fabric

## Slide 3
White Box Switch
Accton 6712
Leaf Switch
24 x 40G ports downlink to servers
8 x 40G ports uplink to different spine switches
ECMP across all uplink ports
GE mgmt.
White Box Switch
Accton 6712
Spine Switch
32 x 40G ports downlink to leaf switches
GE mgmt.
BRCM ASIC
OF-DPA
Indigo OF Agent
OpenFlow 1.3
OCP: Open Compute Project
ONL: Open Network Linux
ONIE: Open Network Install Environment
BRCM: Broadcom Merchant Silicon ASICs
OF-DPA: OpenFlow Datapath Abstraction
Leaf/Spine Switch Software Stack
to controller
OCP
Software
(ONL,ONIE)
OCP Bare Metal Hardware
Disaggregation 1/2 – Bare-metal + Open-Source

## Slide 4
L2 bridged
L3 routed
Disaggregation 2/2– Bare-metal + Open-Source + SDN
Access & Trunk VLANs
IPv4 & IPv6 & MPLS SR
IPv4 Multicast (PIM)
DHCP relay (IPv4)
vRouter BGP/OSPF (ext.)
IPv4 multicast
ONOS Cluster
Notes: Fabric true underlay – never sees vxlan encapsulated addrs
IP down to ToR redundant ToRs
Scales better
Fabric for other purposes

## Slide 5
Ingress
Port Table
Phy Port
Vlan Table
Termin-ation MAC
Table
Multi-
cast Routing Table
Unicast
Routing
Table
MPLS
Table
Bridging
Table
ACL
Policy
Table
L2 Flood
Group
L3 ECMP
Group
Phy Port
Phy Port
Phy Port
Phy Port
Phy Port
MPLS
Label
Group
MPLS
Label
Group
L3
Mcast
Group
L2 Interface
Group
L2 Interface
Group
Fabric ASIC Pipeline* (BRCM’s OF-DPA)
Vlan 1 Table
MPLSL2 Port
Table
* Simplified view
Allows programming of all
flow-tables & port-groups
via OpenFlow 1.3
Why OF-DPA?
OF 1.0
L2 Interface
Group
Phy Port
L2 Interface
Group
OF 1.3
Achieves Dataplane Scale
Notes: Talk about data plane scale

## Slide 6
Switch
Switch
Switch
SDN
Controller
1. Dataplane packets need to go to controller
Reality: Application designs mode of operation!
Fabric control application designed such that dataplane packets never have to go to the controller.
2. Controllers are out-of-net (management stations)
Reality: Controllers are Network Elements (NEs)!
Need to design for redundancy and scale to achieve production readiness
Classic SDN Myths

## Slide 7
Outline
Example Disaggregated Network
High Availability in Disaggregated Networks
Control plane redundancy
Data plane redundancy
Combined data-plane & control-plane failure recovery
Dual-homing servers
vRouter HA
Headless fabric
Open-source, SDN-based
Datacenter Leaf-Spine Fabric

## Slide 8
Redundancy in Networking
ToR switches
Aggregation
Core
Doubled Core Switches;
Spanning tree used
1 + 1 redundancy
“Cisco Normal Form”
Standard Cisco Design.
In most of networking
  2 is a golden number ( 1+1, 1:1, N:1 )
  Acceptible risk/reward – what happens when both routers/switches die – customer network down – low probability, unlikely event
CE
PE
PE

## Slide 9
SDN Controller
R,E,M-Access
Metro
Router
ONOS Controller Cluster
vRouter
Control
vOLT
Control
Overlay
Control
Underlay Control
Multicast
Control
vSG
vSG
vSG
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
OVS
OVS
OVS
OVS
OVS
3
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
Open Source
SDN-based
Bare-metal
White Box
White Box
Tend to show SDN controller as out-of-the-box
But then it’s treated like a management system
  As a workstation outside of the network.
  No management system is HA – if it dies, reboot it
  In the meantime network should still work!

## Slide 10
Reality: Controllers are NEs
R,E,M-Access
Metro
Router
vSG
vSG
vSG
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
OVS
OVS
OVS
OVS
OVS
3
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
Open Source
SDN-based
Bare-metal
White Box
White Box
ONOS Controller Cluster
Need to think of SDN Controller as Network Element (NE)
  And like most networking solutions to redundancy, some SDN solutions do 1:1
  ONOS does much much more
    3-way, 5-way, 7-way redundancy
    Bonus: scales the same way
  Spread instances around in DC racks – N-Way redundancy
    Unlikely event that they all die simultaneously - there are bigger issues if that happens
    Can design for headless mode

## Slide 11
ONOS N-Way Redundancy
ONOS Instance 1
ONOS Instance 2
ONOS Instance 3
ONOS Instance 4
ONOS Instance 5
M
B
B
M
B
B
M
M
B
B
B
B
M
M
B
B
B
B
B
B
M
M
B
B
Switches simultaneously connect to several controller instances.
only 1 controller instance is master, several other instances are backups
Mastership is decided by controllers
Switches have no say
Controller instances simultaneously connect to several switches.
Any controller instance can be master or backup for any switch
Spreading mastership over controller instances contributes to scale
M
B
= Master
= Backup

## Slide 12
ONOS N-Way Redundancy
ONOS Instance 1
ONOS Instance 2
ONOS Instance 3
ONOS Instance 4
ONOS Instance 5
M
B
M
B
M
B
B
M
B
M
B
Switches simultaneously connect to several controller instances.
only 1 controller instance is master, several other instances are backups
Mastership is decided by controllers
Switches have no say
Controller instances simultaneously connect to several switches.
Any controller instance can be master or backup for any switch
Spreading mastership over controller instances contributes to scale
M
B
= Master
= Backup
= Retry
R
R
R
R
M
M
R
R
M
Losing controller instances redistributes switch mastership
Switches continue to retry lost connections
Management watchdog can reboot lost
controller instances

## Slide 13
State Synch: Authoritative State
ONOS Instance 1
ONOS Instance 2
ONOS Instance 3
ONOS Instance 4
ONOS Instance 5
Liveness information (up/down)
Statistics
State:
Network Topology
Network Configuration
Mastership Assignment
FlowRules / Groups
Resource Allocations
Intents
And many more
Observe
Program/Enforce
ONOS instances & apps actively synchronize with each other using state-of-the-art, fault-tolerant distributed systems algorithms
To the external world the cluster behaves like a single logical entity
FlowRules
Groups
Virtual Ports
Mastership

## Slide 14
ONOS Cluster Features
Failures are the rule not exception.
All critical information is 3-way replicated and persisted. Simple configuration change to enable even higher degrees of replication (if needed).
Logically consistent view of replicated state via state of the art distributed consensus and synchronization protocols.
  Raft Consensus for Resources, Mastership, Network Config, …
  Primary/Backup for Flow Rules
  Optimistic Replication for Topology, Data plane stats, …
Failure handling is fully automated.
Workload is evenly distributed. When one node fails, others take over its responsibilities

## Slide 15
Outline
Example Disaggregated Network
High Availability in Disaggregated Networks
Control plane redundancy
Data plane redundancy
Combined data-plane & control-plane failure recovery
Dual-homing servers
vRouter HA
Headless fabric
Open-source, SDN-based
Datacenter Leaf-Spine Fabric

## Slide 16
Data Plane Failures – Losing a Link
Leaf Switch
Leaf Switch
Spine Switch
Spine Switch
ECMP group
ECMP group
Port removed by hardware due to loss of signal
Port removed by fabric-control app on ONOS

## Slide 17
Data Plane Failures – Losing a Link
Leaf Switch
Leaf Switch
Spine Switch
Spine Switch
ECMP group
ECMP group
Port removed by hardware due to loss of signal
ECMP groups
ECMP groups

## Slide 18
Data Plane Failures – Losing a Spine
Leaf Switch
Leaf Switch
Spine Switch
Spine Switch
ECMP group
ECMP group
Port removed by hardware due to loss of signal

## Slide 19
Data Plane Failures – Losing a Leaf
Leaf Switch
Leaf Switch
Spine Switch
Spine Switch
ECMP group
ECMP group
Port removed by hardware due to loss of signal
ECMP groups
ECMP groups
Leaf Switch
Leaf Switch

## Slide 20
Data Plane Failures
Spine Switch
Spine Switch
ECMP group
ECMP group
ECMP groups
ECMP groups
Leaf Switch
Leaf Switch
Leaf Switch
Leaf Switch
With dual-ToRs, dual-uplinks to same spine, and the use of hash-groups,
all single data-plane failures can be handled entirely in hardware without the involvement of the controller

## Slide 21
Outline
Example Disaggregated Network
High Availability in Disaggregated Networks
Control plane redundancy
Data plane redundancy
Combined data-plane & control-plane failure recovery
Dual-homing servers
vRouter HA
Headless fabric
Open-source, SDN-based
Datacenter Leaf-Spine Fabric

## Slide 22
Combined DP & CP Failures
Leaf Switch
Leaf Switch
Spine Switch
Spine Switch
ONOS Instance 1
ONOS Instance 2
ONOS Instance 3
M
M
M
M

## Slide 23
Combined DP & CP Failures
Leaf Switch
Leaf Switch
Spine Switch
Spine Switch
ONOS Instance 1
ONOS Instance 2
ONOS Instance 3
M
M
M
M
Any state needed by the new master to control the switch has already been shared by the app via ONOS distributed stores

## Slide 24
Combined DP & CP Failures
Leaf Switch
Leaf Switch
Spine Switch
Spine Switch
ONOS Instance 1
ONOS Instance 2
ONOS Instance 3
M
M
M
M
Any subsequent dataplane failure is handled by new master

## Slide 25
Outline
Example Disaggregated Network
High Availability in Disaggregated Networks
Control plane redundancy
Data plane redundancy
Combined data-plane & control-plane failure recovery
Dual-homing servers
vRouter HA
Headless fabric
Open-source, SDN-based
Datacenter Leaf-Spine Fabric

## Slide 26
OOB non-SDN
Network
2-way Redundancy Everywhere Else
ToR (Leaf 1)
ToR (Leaf 2)
Access Equipment
Upstream
Router
Spine 1
Spine M
min(#Spines, #ToR-uplink-ports)
GE L2 Mgmt. Switch
GE L2 Mgmt. Switch
ONOS 1
ONOS 2
ONOS N
Upstream
Router
Dual homing upstream routers and using multiple Quaggas
Dual Management ports not available currently

## Slide 27
Server Dual Homing
Leaf Switch
Server
Server
Leaf (ToR) Pair:: same Rack
Leaf Switch
Same subnet (== vlan)
Linux bonding
active-active
Server
Bridging:
Unicast & Broadcast traffic
Redirection over pair-link in the event of failure
Routing:
Access port failure handled as a localized change (using pair-link)
Does not require rerouting elsewhere in the fabric.

## Slide 28
Outline
Example Disaggregated Network
High Availability in Disaggregated Networks
Control plane redundancy
Data plane redundancy
Combined data-plane & control-plane failure recovery
Dual-homing servers
vRouter HA
Headless fabric
Open-source, SDN-based
Datacenter Leaf-Spine Fabric

## Slide 29
vRouter as a VNF?
Dataplane
Control Plane
(OSPF, BGP ..)
Management (CLI, SNMP, NetCONF)
Control Plane
(OSPF, BGP ..)
Dataplane
Management (CLI, SNMP, NetCONF)
VNF = vRouter VM
(vCPE, vBNG,
vPGW, vBRAS)
CP
DP
vRouter
VM
Underlay Network
VNF
VNF
VNF
Issues: Hairpinning
Embedded control plane complicates scale-out
VNFM
(VNF Manager)
DP
DP
DP
DP
DP
CP
Issue: Still hairpinning through a load-balancer
vRouter in Software?

## Slide 30
ONOS Controller Cluster
ONOS Controller Cluster
VM
VM
Trellis vRouter
Underlay Control
OSPF
I-BGP
vRouter app
Quagga
(or other)
Router
Router
External
ONOS
Overlay Control
OVS
OVS
VNF
VNF
OVS
OVS
vRouter Operation

## Slide 31
ONOS Controller Cluster
ONOS Controller Cluster
VM
VM
Trellis vRouter
Underlay Control
OSPF
I-BGP
vRouter
Quagga
(or other)
Router
Router
ONOS
Overlay Control
OVS
OVS
VNF
VNF
OVS
OVS
External
vRouter Operation

## Slide 32
ONOS Controller Cluster
ONOS Controller Cluster
VM
VM
Underlay Control
OSPF
I-BGP
vRouter
Quagga
(or other)
Router
Router
ONOS
Overlay Control
OVS
OVS
VNF
VNF
OVS
OVS
External
vRouter Operation

## Slide 33
vRouter Dual-Homing
NA
NB
2
1
2
1
NA
NB

## Slide 34
vRouter Dual-Homing
Spine Switch
Spine Switch
Q
Q
ONOS Instance 1
ONOS Instance 2
ONOS Instance 3
FPM
Connections
NA
NB
P1NA1
P1NB1
P1NA2
P1NB2
P1NA1
P1NB2
2
1
2
1
P1-> 201,202
P1NA1 -> p1
P1NB2 -> p2
P1-> 201,202

## Slide 35
Outline
Example Disaggregated Network
High Availability in Disaggregated Networks
Control plane redundancy
Data plane redundancy
Combined data-plane & control-plane failure recovery
Dual-homing servers
vRouter HA
Headless fabric
Open-source, SDN-based
Datacenter Leaf-Spine Fabric

## Slide 36
Headless Mode
Physical or Virtual Switch
Connected End-Point
(VM, container, server,
router, PNF etc.)
ONOS Instance
ARP handler app
ARP request
ARP reply
Physical or Virtual Switch
Connected End-Point
(VM, container, server,
router, PNF etc.)
ONOS Instance
ARP
delegation app
ARP request
ARP reply
ARP agent
ARP delegation

## Slide 37
Summary
Disaggregated Network – Bare-metal + Open-source + SDN-based Leaf-Spine Fabric
  Vlan, IPv4, IPv6, MPLS SR, IPv4 Multicast, DHCP Relay, vRouting
ONOS is a Network Element, not a management station
  ONOS strength: N-way redundancy & scale
  3R recovery: Redistribute mastership, Retry connections, Reboot instances
  Low probability of all controller instances dying simultaneously
2-way redundancy everywhere else
  Dual-ToRs, Servers-to-ToRs, Routers-to-ToRs, Access-to-ToRs, Dual-management ports
  Acceptable in most/all networking scenarios
Headless mode: in the unlikely event that all controllers are lost
  Existing network & services continue to operate as before
    Even if there are subsequent data-plane failures
    Requires dual uplinks to same spine, local agents for ARP delegation, and pair-link reroute.
  New services, subscribers and routes, hosts (dhcp) cannot be provisioned
    Acceptable/tolerated in interim state