## Slide 1
Trellis Update
Saurav Das
Principal Architect, ONF
With contributions from many others …

## Slide 2: What is Trellis?
Datacenter Leaf-Spine Fabric Underlay
Virtual Network Overlay
Unified SDN Control
Of Underlay & Overlay
ONOS
Controller Cluster & Apps
Trellis is the enabling Network Infrastructure for CORD
Trellis Provides Common control over underlay & overlay networks, including
Service Composition for Tenant Networks
Distributed Virtual Routing
Optimized Delivery of Multicast Traffic Streams

## Slide 3: CORD Architecture
R,E,M-Access
Access
Links
ONOS
vRouter
Other Apps
Overlay
Control
Underlay Control
Other
Apps
XOS
vSG
vSG
vSG
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
OVS
OVS
OVS
OVS
OVS
3
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
TRELLIS
Metro
Router

## Slide 4
White Box Switch
Accton 6712
Leaf Switch
24 x 40G ports downlink to servers
8 x 40G ports uplink to different spine switches
ECMP across all uplink ports
GE mgmt.
White Box Switch
Accton 6712
Spine Switch
32 x 40G ports downlink to leaf switches
GE mgmt.
BRCM ASIC
OF-DPA
Indigo OF Agent
OpenFlow 1.3
OCP: Open Compute Project
ONL: Open Network Linux
ONIE: Open Network Install Environment
BRCM: Broadcom Merchant Silicon ASICs
OF-DPA: OpenFlow Datapath Abstraction
Leaf/Spine Switch Software Stack
to controller
OCP
Software
(ONL,ONIE)
OCP Bare Metal Hardware
Disaggregation – Bare-metal + Open-Source

## Slide 5
L2 bridged
L3 routed
Trellis Fabric – Bare-metal + Open-Source + SDN
Access & Trunk VLANs
IPv4 & IPv6 & MPLS SR
IPv4 Multicast (PIM)
DHCP relay (IPv4)
vRouter BGP/OSPF (ext.)
IPv4 multicast
ONOS Cluster
Notes: Fabric true underlay – never sees vxlan encapsulated addrs
IP down to ToR redundant ToRs
Scales better
Fabric for other purposes

## Slide 6
vRouter as a VNF?
Dataplane
Control Plane
(OSPF, BGP ..)
Management (CLI, SNMP, NetCONF)
Control Plane
(OSPF, BGP ..)
Dataplane
Management (CLI, SNMP, NetCONF)
VNF = vRouter VM
(vCPE, vBNG,
vPGW, vBRAS)
CP
DP
vRouter
VM
Underlay Network
VNF
VNF
VNF
Issues: Hairpinning
Embedded control plane complicates scale-out
VNFM
(VNF Manager)
DP
DP
DP
DP
DP
CP
Issue: Still hairpinning through a load-balancer
vRouter in Software?

## Slide 7
ONOS Controller Cluster
ONOS Controller Cluster
VM
VM
Trellis vRouter
Underlay Control
OSPF
I-BGP
vRouter app
Quagga
(or other)
Router
Router
External
ONOS
Overlay Control
OVS
OVS
VNF
VNF
OVS
OVS
vRouter Operation

## Slide 8
ONOS Controller Cluster
ONOS Controller Cluster
VM
VM
Trellis vRouter
Underlay Control
OSPF
I-BGP
vRouter
Quagga
(or other)
Router
Router
ONOS
Overlay Control
OVS
OVS
VNF
VNF
OVS
OVS
External
vRouter Operation

## Slide 9
ONOS Controller Cluster
ONOS Controller Cluster
VM
VM
Underlay Control
OSPF
I-BGP
vRouter
Quagga
(or other)
Router
Router
ONOS
Overlay Control
OVS
OVS
VNF
VNF
OVS
OVS
External
vRouter Operation
Trellis vRouter  Implemented as a big distributed router
 Presents entire n/w infrastructure as a single router to outside world
Trellis vRouter  Implemented as a big distributed router
 Presents entire n/w infrastructure as a single router to outside world
Trellis vRouter  Implemented as a big distributed router
 Presents entire n/w infrastructure as a single router to outside world
Trellis vRouter  Implemented as a big distributed router
 Presents entire n/w infrastructure as a single router to outside world
Trellis vRouter  Implemented as a big distributed router
 Presents entire n/w infrastructure as a single router to outside world
Trellis vRouter  Implemented as a big distributed router
 Presents entire n/w infrastructure as a single router to outside world
Trellis vRouter  Implemented as a big distributed router
 Presents entire n/w infrastructure as a single router to outside world

## Slide 10
Current Work - Data Plane Redundancy
Spine Switch
Spine Switch
ECMP group
ECMP group
ECMP groups
ECMP groups
Leaf Switch
Leaf Switch
Leaf Switch
Leaf Switch
Access Equipment
Upstream
Router
Upstream
Router

## Slide 11
Roadmap
See here for complete roadmap
https://docs.google.com/spreadsheets/d/1SmKxsZ9iHtLHoEtvsntsJ98tLf_cYT_qXuuO7eAUtt4/edit?usp=sharing