## Slide 1
#OpenCORD
TRELLIS
CORD Network Infrastructure Saurav Das
… with Ali Al-Shabibi, Jonathan Hart, Hyunsun Moon, Charles Chan & Flavio Castro
Photo source: Wikipedia

## Slide 2
What is Trellis?
1. DC Leaf-Spine Fabric Underlay
2. Virtual Network Overlay
3. Unified SDN Control
over underlay & overlay
ONOS
Controller Cluster & Apps
Unique combination of these three components
Trellis is the enabling Network Infrastructure for CORD
Trellis Benefits
Common control over underlay & overlay networks enable simple, efficient impls of:
Distributed Virtual Routing for tenant networks
Optimized delivery of multicast traffic streams
and many more optimizations & new capabilities to be introduced in the near future

## Slide 3
CORD Architecture
R,E,M-Access
Access
Links
Metro
Router
ONOS Controller Cluster
vRouter
Control
Other Apps
Overlay
Control
Underlay Control
Other
Apps
XOS
vSG
vSG
vSG
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
OVS
OVS
OVS
OVS
OVS
3
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
TRELLIS

## Slide 4
Outline
Underlay Fabric
  Bare-metal + Open-source = White-Box
  L2/L3 Leaf-Spine with SDN Control
Virtual Network Overlay
  OVS and VXLAN with SDN Control
  Service chaining
vRouter
  Distributed Virtual Routing
  Multicast handling
Underlay Fabric
  Bare-metal + Open-source = White-Box
  L2/L3 Leaf-Spine with SDN Control
Virtual Network Overlay
  OVS and VXLAN with SDN Control
  Service chaining
vRouter
  Distributed Virtual Routing
  Multicast handling

## Slide 5
White Box SDN Switch
Accton 6712
Leaf Switch
24 x 40G ports downlink to servers
and OLTs
8 x 40G ports uplink to different spine switches
ECMP across all uplink ports
GE mgmt.
White Box SDN Switch
Accton 6712
Spine Switch
32 x 40G ports downlink to leaf switches
40G QSFP+/DAC
GE mgmt.
BRCM ASIC
OF-DPA
Indigo OF Agent
OF-DPA API
OpenFlow 1.3
OCP: Open Compute Project
ONL: Open Network Linux
ONIE: Open Network Install Environment
BRCM: Broadcom Merchant Silicon ASICs
OF-DPA: OpenFlow Datapath Abstraction
Leaf/Spine Switch Software Stack
to controller
OCP
Software
-
ONL
ONIE
OCP Bare Metal Hardware
Underlay Fabric: Open Hardware & Software Stacks
BRCM SDK API

## Slide 6
L2 bridged
IPv4 unicast / MPLS SR
Underlay Fabric Operation
Notes: Fabric true underlay – never sees vxlan encapsulated addrs
IP down to ToR redundant ToRs
Scales better
Fabric for other purposes

## Slide 7
Ingress
Port Table
Phy Port
Vlan Table
Termin-ation MAC
Table
Multi-
cast Routing Table
Unicast
Routing
Table
MPLS
Table
Bridging
Table
ACL
Policy
Table
L2 Flood
Group
L3 ECMP
Group
Phy Port
Phy Port
Phy Port
Phy Port
Phy Port
MPLS
Label
Group
MPLS
Label
Group
L3
Mcast
Group
L2 Interface
Group
L2 Interface
Group
Underlay Fabric ASIC Pipeline* (BRCM’s OF-DPA)
Vlan 1 Table
MPLSL2 Port
Table
* Simplified view
Allows programming of
all flow-tables & port-groups
via OpenFlow 1.3
Why OF-DPA?
OF 1.0
L2 Interface
Group
Phy Port
L2 Interface
Group
OF 1.3
Achieves Dataplane scale
Notes: Talk about data plane scale

## Slide 8
Switch
Switch
Switch
SDN
Controller
Classic-SDN Myths:
1. Dataplane packets need to go to controller
Reality: Application designs mode of operation!
Fabric control application designed such that dataplane packets never have to go to the controller.
2. Controllers are out-of-the-network, like management stations
Reality: Controllers are Network Elements (NEs)!
Almost all NE redundany is 1:1 or 1+1 (2-way redundancy)
ONOS does much, much more
  3-way, 5-way, 7-way redundancy
  Bonus: scales the same way
Control Plane HA, Scale & Performance

## Slide 9
ONOS Instance 1
ONOS Instance 2
ONOS Instance 3
ONOS Instance 4
ONOS Instance 5
M
B
B
M
B
B
M
M
B
B
B
B
M
M
B
B
B
B
B
B
M
M
B
B
Switches simultaneously connect to several controller instances.
only 1 controller instance is master, several other instances are backups
Mastership is decided by controllers
Switches have no say
Controller instances simultaneously connect to several switches.
Any controller instance can be master or backup for any switch
Spreading mastership over controller instances contributes to scale
M
B
= Master
= Backup
ONOS N-Way Redundancy

## Slide 10
ONOS Instance 1
ONOS Instance 2
ONOS Instance 3
ONOS Instance 4
ONOS Instance 5
M
B
M
B
M
B
B
M
B
M
B
Spreading mastership over controller instances contributes to scale
M
B
= Master
= Backup
= Retry
R
R
R
R
M
M
R
R
M
Losing controller instances redistributes switch mastership
Switches continue to retry lost connections
Management watchdog can reboot lost
controller instances
ONOS N-Way Redundancy
Switches simultaneously connect to several controller instances.
only 1 controller instance is master, several other instances are backups
Mastership is decided by controllers
Switches have no say
Controller instances simultaneously connect to several switches.
Any controller instance can be master or backup for any switch

## Slide 11
Outline
Underlay Fabric
  Bare-metal + Open-source = White-Box
  L2/L3 Leaf-Spine with SDN Control
Virtual Network Overlay
  OVS and VXLAN with SDN Control
  Service chaining
vRouter
  Distributed Virtual Routing
  Multicast handling
Underlay Fabric
  Bare-metal + Open-source = White-Box
  L2/L3 Leaf-Spine with SDN Control
Virtual Network Overlay
  OVS and VXLAN with SDN Control
  Service chaining
vRouter
  Distributed Virtual Routing
  Multicast handling

## Slide 12
OVS
OVS
OVS
OVS
OVS
OVS
OVS
OVS
OVS
Virtual Network Overlay
VXLAN Overlay
VXLAN Overlay
VXLAN
Overlay
Tenant Green
Virtual Network
Tenant Red
Virtual Network
Service Y
Virtual Network
Service B
Virtual Network
VMs/Containers
Single VXLAN
port in OvS
Overlapping address space
Connectivity isolation
Service VNFs & vNets
Non-overlapping addresses
Services can dynamically
grow or shrink
Notes: Any server virtualization tech – VMs or containers, KVM or Docker or LXC
Single OVS bridge with VXLAN overlays – only use VXLAN dataplane encapsulation, no control plane associated with vxlan is used
Single VXLAN port – tunnel destination is added dynamically
Tenant virtual networks– tenant VMs/containers can be anywhere in the cloud, have overlapping IP address space and connectivity isolation from each other – minimum expectation for virtual networking
Services (VNFs) are also tenants of the cloud – each service is instantiated by multiple containers or VMs and each service has its own vnet
Services can dynamically grown and shrink – in compute & networking
Service vnets cannot have overlapping address space.

## Slide 13
OVS
OVS
OVS
OVS
OVS
OVS
OVS
OVS
OVS
Service Composition Impl
VXLAN Overlay
VXLAN
Overlay
Tenant Green
Virtual Network
Service Y
Virtual Network
Service B
Virtual Network
Service graph is created by XOS and programmed into OvS by overlay-control app (VTN)
XOS
VTN
ONOS
Service-graph
OpenFlow
rules
Service P
Virtual Network
Distributed load-balancers exist for each service in each OvS
Notes: Eample service graph – where service Y asks for another service – is that part of graph as well?
Services are interconnected by distributed load-balancers
Can you bounce off a router – standard openstack?
Service graph vs neutron

## Slide 14
OVS Pipeline* (Vnets & Service-Chaining)
Incoming
Lookup
(port, vlan, arp)
QinQ
lookup
Next
Service
Lookup/Tenant VRFs
Service
Load
Balancing / Service IP Lookup
VXLAN Encap
VxLAN VNI
Lookup & Decap
to vSG or OLT
to
Underlay
Fabric
VM/Container
Lookup
To local
Service Instance
to controller
All flow-tables & port-groups are programmed using OpenFlow 1.3
VxLAN tunnel ports are created using OVSDB protocol
Ingress
Pipeline
from underlay
fabric
* Simplified view
Egress
pipeline

## Slide 15
Leaf
Spine
Leaf
OVS
MAC DA
of Service 2
MAC SA
of S1B
Payload
MAC DA
spine
MAC SA
leaf
SR Label of dst leaf sw
OVS IP addrs infra
UDP
VXLAN
VNI=S2
MAC DA
of S2C
MAC SA
of S1B
MAC DA
of S2C
MAC SA
of S1B
Dst IP lookup, SR label-push
& load-balancing to spines
Underlay Fabric
Server
Server
S1B
OVS
S2C
MAC DA
Leaf
MAC SA
OVS
OVS IP addrs infra
UDP
VXLAN
VNI=S2
MAC DA
of S2C
MAC SA
of S1B
MAC DA
leaf
MAC SA
spine
OVS IP addrs infra
UDP
VXLAN
VNI=S2
MAC DA
of S2C
MAC SA
of S1B
Tunnel encap & load-balancing to next Service instances
MAC DA
OVS
MAC SA
leaf
OVS IP addrs infra
UDP
VXLAN
VNI=S2
MAC DA
of S2C
MAC SA
of S1B
IPSrc= Cust.IP
IPDst= World
or opposite
Payload
Payload
Payload
Payload
Payload
SR Label lookup, pop & forward to destination leaf
Dst IP lookup & forward to destrination server
Tunnel decap
IPSrc= Cust.IP
IPDst= World
or opposite
IPSrc= Cust.IP
IPDst= World
or opposite
IPSrc= Cust.IP
IPDst= World
or opposite
IPSrc= Cust.IP
IPDst= World
or opposite
IPSrc= Cust.IP
IPDst= World
or opposite
Trellis Overlay & Underlay
VXLAN Overlay

## Slide 16
Outline
Underlay Fabric
  Bare-metal + Open-source = White-Box
  L2/L3 Leaf-Spine with SDN Control
Virtual Network Overlay
  OVS and VXLAN with SDN Control
  Service chaining
vRouter
  Distributed Virtual Routing
  Multicast handling
Underlay Fabric
  Bare-metal + Open-source = White-Box
  L2/L3 Leaf-Spine with SDN Control
Virtual Network Overlay
  OVS and VXLAN with SDN Control
  Service chaining
vRouter
  Distributed Virtual Routing
  Multicast handling

## Slide 17
vRouter as a VNF?
Dataplane
Control Plane
(OSPF, BGP ..)
Management (CLI, SNMP, NetCONF)
Control Plane
(OSPF, BGP ..)
Dataplane
Management (CLI, SNMP, NetCONF)
VNF = vRouter VM
(vCPE, vBNG,
vPGW, vBRAS)
CP
DP
vRouter
VM
Underlay Network
VNF
VNF
VNF
Issues: Hairpinning, Embedded control plane complexity for scale-out
VNFM
(VNF Manager)
DP
DP
DP
DP
DP
CP
Issues: Still hairpinning through a load-balancer appliance
Trellis vRouter takes
a different approach

## Slide 18
ONOS Controller Cluster
ONOS Controller Cluster
OLT
OLT
OLT
To residential
subscribers
VM
VM
Trellis vRouter
Underlay Control
OSPF
I-BGP
vRouter Control
Quagga
(or other)
Router
Router
Upstream
Metro network
ONOS Controller Cluster
XOS
Overlay Control
OVS
OVS
VNF
VNF
OVS
OVS
Trellis vRouter  Implemented as a big distributed router
 Presents entire n/w infrastructure as a single router to outside world

## Slide 19
ONOS Controller Cluster
ONOS Controller Cluster
ONOS Controller Cluster
OLT
OLT
OLT
To residential
subscribers
vSG
vSG
IPv4 multicast video
Optimized Multicast in R-CORD
Underlay Control
Multicast Control
IGMP
Snooping
PIM-SSM
Router
Router
Upstream
Metro network
XOS
R-CORD Multicast video streams never need to go through any software switch or VNF

## Slide 20
Trellis Summary
Designed for NFV (service-chained VNFs) with best principles of cloud
  Orchestration, agility, elasticity, micro-services
Overlay control application (VTN) implements/maintains service graph presented by XOS
  SDN control plane – mostly proactive, HA, no distributed protocols
  Designed to scale up to 400 virtual switches
OvS + VXLAN data plane
  Standard VXLAN dataplane encap/decap with entropy-hashing
  Custom OvS pipeline for tenant virtual networks, service-chaining & per-service load-balancing
Underlay Fabric
Virtual Network Overlay
Unified SDN Control
TRELLIS: DC Fabric Underlay + Virtual Network Overlay + Unified SDN Control
L2/L3 spine-leaf fabric built on bare-metal hw and open-source software
  Preferred architecture in modern DCs: horizontal scaling & high bisection bandwidth
  Designed to scale up to 16 racks (~ 40 hardware switches)
  Low cost ~ $5k per switch
SDN control plane - no distributed protocols
  Proactive mode of operation
  Highly available & scalable – ONOS N-way control plane redundancy & scale
Modern ASIC data plane - 1.28 Tbps switching bandwitdth for each switch
  Broadcom’s OF-DPA + OpenFlow 1.3 use of multi-tables & port-groups => dataplane scale
Common control provides opportunites for optimized service delivery
    vRouter – Distributed routing using SDN control and hardware fabric
    Multicast IPTV service delivery in R-CORD
    More to follow

## Slide 21
BACKUP

## Slide 22
CORD Infrastructure Choices: #Racks
Source: Ciena
CORD comes in many sizes  Suitable for many different deployment scenarios
 Underlay leaf-spine fabric is designed to scale horizontally

## Slide 23
CORD Infrastructure Choices: Underlay Fabric
White Box SDN
Grey Box SDN
White Box Td
Grey Box Td
Black Box Td
Open Source SDN Software on Bare-Metal Hardware
Proprietary SDN Software on Bare-Metal Hardware
Open Source Traditional n/w Software on Bare-Metal Hardware
ProprietaryTraditional n/w Software on Bare-Metal Hardware
ProprietaryTraditional n/w Software on Proprietary Hardware
Open Source SDN Software
* OF-DPA API
* ONL
* Indigo
Bare Metal Hardware Choices
* Accton
* Delta
* Dell
* Wedge
* Quanta
* Interface Masters
* Celestica
Dell
* Dell/DNI hardware
* OF-DPA
* FTOS / OS10
BigSwitch
* Switch Light OS
* Most bare-metal hw
Pica8
* PicOS
* Most bare-metal hw
Google
* Jupiter fabric
OpenSwitch
* HP initiative
* Most bare-metal hw
SONIC
* Microsoft initiative
* Most bare-metal hw
FBOSS
* Facebook initiative
* Wedge hw
Cumulus
* Cumulus Linux
* Most bare-metal hw
Pluribus
* Netvisor software
* Freedom bare-metal hw
LinkedIn
* Pigeon switch
* Bare metal hw
Broadcom
* FastPath software
* Bare metal hw
Cisco
& others
CORD uses White Box SDN  1) Simpler 2) Easier to introduce new features 3) Lower TCO
+ Significant advantages of common SDN control over underlay and overlay.
Progressively less agile, slower innovation, more complex as we move from Left  Right

## Slide 24
CORD Infrastructure Choices: Software Switches
Two choices: OVS + DPDK
BESS + DPDK
Chart: Tput @ 64B (Phy-vSwitch-Phy)
| 1 core | 2 cores | 4 cores
OVS-DPDK | 16766108.36 | 30347400.485 | 47266489.816
BESS | 36389993.489 | 59523789.937 | 59523795.607
Open Questions:
  How do both perform with VxLAN encap?
  And do more than simple bridging?
Source: Joshua Reich, AT&T

## Slide 25
...
...
CORD System: Access Choices
Remote leafs can be managed in-band by ONOS at CO node
Remote leafs perform
  Aggregation of ‘pizza-box’ OLT traffic
    Assumes transport equipment can deliver double-vlan tagged Ethernet frames from remote-leaf to CO
  Encapsulation of frames (if necessary)
    E-Lines implemented using MPLS PW
PON
OLTs
Optical Transport / Carrier Ethernet
Remote leafs
PON
OLTs

## Slide 26
CORD System: Metro Choices
...
...
Traditional
IP/MPLS Network
BGP/OSPF
Multiple Central Offices
...
...
...
...

## Slide 27
Trellis Roadmap
Q2’16
CORD 1st Release
XOS
ONOS
Underlay
Overlay
Multicast
vOLT
vRouter
vSG
Accton
Celestica
OF-DPA
ONL
Indigo
Quagga
OVS
Dual Homing
Servers to 2 ToRs
OLTs to 2 TorRs
ToRs to 2 Upstream routers
DPDK + OVS/BESS
with VxLAN
and VTN pipeline
More VNFs
Closed & Open source
Different service chains
ISSU
ARP Delegation
Troubleshooting Tools
Everywhere
sFlow Integration
Scale Testing
Users, switches, servers
PNF Integration
Leaf VTEP
Remote Field Office
Requires in-band control
Inter Central Office
More Integration
E-CORD & M-CORD
IPv6
Flat
network
P4
More Access Intr.
G.Fast & other vendors
Plat-forms
Apps
VNF
Hw
Switch
software
VTN options

## Slide 28
CORD System: PNFs
ONOS Cntroller Cluster
ONOS Controller Cluster
ONOS Controller Cluster
OLT
OLT
OLT
To residential
subscribers
VNF
vSG
Underlay Control
Overlay Control
Router
Router
Upstream
Metro network
XOS
CORD Service graphs are implemented by both overlay & underlay fabrics
PNF
OVS
OVS
OVS

## Slide 29
ToR switches
Aggregation
Core
Cisco “normal” design
Spanning tree used
1 + 1 redundancy
Why DC Leaf-Spine Fabrics?
Old design not good for east-west (dominant) traffic in modern data-centers

## Slide 30
Why Bare Metal Switches?
DRAM
CPU
Power supply + fans
Linux
xChip
Optional Remote API
ONL, SwitchLight, PicOS, FBOSS, SONIC, OpenSwitch, Cumulus, Pigeon, FastPath, SnapRoute
API/Driver
OF-DPA, OpenNSL, SAI, P4
ONIE
Boot Loader
Accton
Delta
Dell
Wedge
Quanta
Interface Masters
Celestica
Cost
400,000 servers
20,000 switches
$5k vendor switch = $100M
$1k bare-metal switch = $20M
Savings in 10 data centers = $800M
Control
Tailor network to applications
Proprietary behavior
Quickly debug
No vendor lock-in

## Slide 31
Simpler Control with Greater Flexibility
  Networks work because we can master complexity, but what we should be doing is extracting simplicity, with the right abstractions
Speed of Innovation, Ease of Service Insertion & Faster Time to Market
  Does not involve changing/creating a fully distributed protocol
Lower Total Cost of Ownership (TCO)
  Lower Opex – easier to manage, troubleshoot, emulate
  Lower Capex – replacing proprietary hardware
Why SDN?
Benefits of Classic SDN

## Slide 32
Analytics Driven Traffic Engineering

## Slide 33
Policy Driven Traffic Engineering

## Slide 34
Analytics Driven Traffic Engineering