## Slide 1: R-CORD & VOLTHA Introduction
Saurav Das (ONF) & Shawn Ying (AT&T)
CORD Build 2017, San Jose
November 6, 2017

## Slide 2
Economies of a datacenter
  Infrastructure built with a few commodity building blocks using open source software and white-box switches
Agility of a cloud provider
Software platforms that enable rapid creation of new services
Central Office Re-Architected as a Datacenter (CORD) Overview
or… Bringing Access-as-a-Service to the Cloud
SDN
NFV
Cloud
Notes: If you go and talk to service providers around the globe they will tell you they want essentially two things:
1. Economies of a data center
2. Agility of a cloud provider
Each service provider may articulate it differently but it comes down to these two high level requirements.
What do these requirements mean?
This means service providers want to build their infrastructure like the datacenters – that is build it using a few commodity building blocks that use open source software and hardware.
For example datacenters use commodity servers, white boxes for the leaf and spine switches, and many open source software platforms and tools.
The net result is that the service providers can scale their infrastructure and significantly reduce capex and opex.
Agility means they want to introduce new revenue generating services quickly – what cloud providers do so well.
In short this comes down to: reduce expenses and grow revenue
Every business needs to do that, especially service providers given their business realities and compete well with OTT providers.

## Slide 3: CORD: Multi-Access Architecture
Access Service Orchestration & Control
Mobile vBBU. vMME, vSGW, vPGW, vCDN
ROADM (Core)
Metro Ethernet
BBUs
PON OLTs
Residential vOLT, vSG, vRouter, vCDN
Enterprise vCarrierEthernet, vOAM, vWanEx, vIDS
COTS (Off-the-Shelf) x86 Compute
White-box Switches with
Merchant Silicon

## Slide 4
ToR
ToR
ToR
Spine
Spine
Spine
ToR
ToR
ToR
ToR
SDN Controller (ONOS Cluster)
Fabric
Control
vOLT
Control
AAA
Control
DHCP
Relay
OpenFlow 1.3
vRouter
Control
…
Bare-metal
Open-source
Leaf-Spine Fabric
ToR
NETCONF
…
CORD Controller (XOS)
Maple
QumranAX
XGS-PON Whitebox OLT
(EdgeCore)
Multi-vendor
ONT/ONUs & RG
VOLTHA
VOLTHA
CDN
vSG
CDN
vSG
Dataplane VNFs in
Edge Compute
Metro Routers
Control Plane VNFs
as SDN apps
Service Creation
and Orchestration
3rd Party Service VNFs
Maple
QumranAX
Residential CORD

## Slide 5: Virtual OLT Hardware Abstraction (VOLTHA)
VOLTHA southbound adapters
Tibit
Tibit Micro-OLT
Ciena
Whitebox OLT (EdgeCore)
Calix
ASFvOLT16
Nokia
Adtran
Nokia
OLT
Adtran OLT
Ciena
OLT
Calix
OLT
fluentd
consul
registrator
adapter_agent
config_proxy
config_root
grpc_server
global_handler
dispatcher
kafka_client
VOLTHA
core
Envoy (REST)
OpenFlow Agent
NetConf agent
VOLTHA
northbound
VOLTHA hides PON-level details (T-CONT, GEM ports, OMCI etc.) from the SDN controller,
and abstracts each PON as a pseudo-Ethernet switch easily programmed by the SDN controller
Common control and management
framework shared by all
OLTs &ONUs
Notes: Common abstraction layer for multiple vendors OLTs and ONUs
VOLTHA core handles PON details
Presents and OF switch abstraction northbound
OLT and ONU adapters are separated with the goal of allowing interop between different vendors
Architected using modern cloud-native principles. Leverages Docker for containerization and different functions run in different docker containers. Docker Swarm for HA

## Slide 6
Whitebox ToR Fabric Switch
CORD Head Node
CORD Compute Node
ONOS
XOS
OpenStack
MAAS
…
VOLTHA
vSG
OvS
EdgeCore 7712 (Tomahawk 32 x 100G)
EdgeCore Whitebox OLT (ASFvOLT16)
Nokia SD-OLT
(LightSpan CF-24W)
Internet
BBWF R-CORD & VOLTHA Demo
Residential Subscribers
Central Office
Nokia
ONU
BCM
ONU
RG
RG

## Slide 7
Whitebox ToR Fabric Switch
CORD Head Node
CORD Compute Node
ONOS
XOS
OpenStack
Radius
…
VOLTHA
vSG
OvS
EdgeCore 7712 (Tomahawk 32 x 100G)
EdgeCore Whitebox OLT (ASFvOLT16)
Nokia SD-OLT
(LightSpan CF-24W)
Internet
802.1x Subscriber Authentication
Residential Subscribers
Central Office
Nokia
ONU
BCM
ONU
RG
RG

## Slide 8
Whitebox ToR Fabric Switch
CORD Head Node
CORD Compute Node
ONOS
XOS
OpenStack
Radius
…
VOLTHA
vSG
OvS
EdgeCore 7712 (Tomahawk 32 x 100G)
EdgeCore Whitebox OLT (ASFvOLT16)
Nokia SD-OLT
(LightSpan CF-24W)
Internet
Subscriber VLAN Provisioning
Residential Subscribers
Central Office
Nokia
ONU
BCM
ONU
RG
RG

## Slide 9
Whitebox ToR Fabric Switch
CORD Head Node
CORD Compute Node
ONOS
XOS
OpenStack
Radius
…
VOLTHA
vSG
OvS
EdgeCore 7712 (Tomahawk 32 x 100G)
EdgeCore Whitebox OLT (ASFvOLT16)
Nokia SD-OLT
(LightSpan CF-24W)
Internet
Subscriber Data-plane Traffic
Residential Subscribers
Central Office
Nokia
ONU
BCM
ONU
RG
RG

## Slide 10
Whitebox ToR Fabric Switch
CORD Head Node
CORD Compute Node
ONOS
XOS
OpenStack
Radius
…
VOLTHA
vSG
OvS
EdgeCore 7712 (Tomahawk 32 x 100G)
EdgeCore Whitebox OLT (ASFvOLT16)
Nokia SD-OLT
(LightSpan CF-24W)
Internet
Subscriber Services
Residential Subscribers
Central Office
Nokia
ONU
BCM
ONU
RG
RG
CDN
Video
Source
Subscriber view
Operator view

## Slide 11
BBWF Booth E107B