## Slide 1: Trellis, Voltha & Residential CORD Saurav Das Director of Engineering, ONF
May 21, 2018

## Slide 2
Multi-purpose leaf-spine
fabric designed for NFV
Bare-metal hardware
Open-source software
SDN-based (built on ONOS)
Trellis Overview

## Slide 3
Bridging with Access & Trunk VLANs (within a rack)
Routing (inter-rack)
  IPv4 & IPv6 Unicast routing with MPLS Segment-Routing
  IPv4 & IPv6 Multicast routing
Dual-homing for compute-nodes and external routers
Multi-stage fabrics (2 layers of spines)
vRouter - entire fabric behaves as a single router
  BGP (v4/v6) support for external (upstream) connectivity
  Static routes, route blackholing
  DHCP L3 relay (IPv4/v6)
MPLS Pseudowires
QinQ termination
T3 - Trellis Troubleshooting Tool
ASIC Support
  Broadcom Qumran, Tomahawk, Trident2 switches from EdgeCore & QCT
  Preliminary support for Cavium Xpliant switches and P4-based Tofino switches
Trellis Features

## Slide 4
White Box Switch
EdgeCore 5712,5912
QCT LY8
Leaf Switch
48 x 10G, 6 x 40G/100G
GE mgmt.
White Box Switch
EdgeCore 6712,7712
Spine Switch
32 x 40G/100G ports downlink to leaf switches
GE mgmt.
BRCM ASIC
OF-DPA
Indigo OF Agent
OpenFlow 1.3
OCP: Open Compute Project
ONL: Open Network Linux
ONIE: Open Network Install Environment
BRCM: Broadcom Merchant Silicon ASICs
OF-DPA: OpenFlow Datapath Abstraction
Leaf/Spine Switch Software Stack
to controller
OCP
Software
(ONL,ONIE)
OCP Bare Metal Hardware
White-Box = Bare-metal hw + Open-Source sw
Trident2, Tomahawk, Qumran

## Slide 5
Ingress
Port Table
Phy Port
Vlan Table
Termin-ation MAC
Table
Multi-
cast Routing Table
Unicast
Routing
Table
MPLS
Table
Bridging
Table
ACL
Policy
Table
L2 Flood
Group
L3 ECMP
Group
Phy Port
Phy Port
Phy Port
Phy Port
Phy Port
MPLS
Label
Group
MPLS
Label
Group
L3
Mcast
Group
L2 Interface
Group
L2 Interface
Group
Fabric ASIC Pipeline* (BRCM’s OF-DPA)
Vlan 1 Table
MPLSL2 Port
Table
* Simplified view
Abstracts underlying ASIC
Enables programming of all
flow-tables & port-groups
Why OF-DPA?
L2 Interface
Group
Phy Port
L2 Interface
Group
Notes: Talk about data plane scale

## Slide 6
ONOS Cluster
P4Runtime
gNMI
Barefoot Tofino
Mellanox
Cavium Xpliant
fabric.p4 driver
Trellis & P4
OF-DPA driver
Brcm Qumran
Brcm Trident2
Brcm Tomahawk
OpenFlow
NetConf
Segment Routing
DHCP L3 Relay
vRouter
Multicast
SPGW-app
Same set of Trellis applications on ONOS
P4
capable hardware
Allowing new functionality on hardware (demo at MWC ‘18)
P4
Enhanced with P4 program deployment and pipeline configuration

## Slide 7
Trellis @ Comcast

## Slide 8
Distributed DevOps – ONF Responsibilities
Report issues found; ~75 cases
Create automated tests to reproduce
Validate fixes / releases
Help with issues in their setup
Design discussions for new features
Daily scrum
Deliver features; meet ops needs
Deliver stability, scale, perf, tools
Support Comcast design/dev/QA teams – issue analysis; root-cause; recommend best-practices/training
Design discussions for new features
Daily scrum
Documentation
Analyse issues reported by Harmonic in their setups
Code review patches they submit to ONOS
Design discussions for new features
Bringing up ONF pod housed in San Jose
Bringing up ONF pod hosted by Flex
QA collaboration
Report issues found in hw
Validate T2 versions of switch software EdgeCore builds for us
Design discussions for apps/features created by Nokia
Code review submitted patches (40 changesets; 4-5 patchsets/change)
Validate some features; report issues

## Slide 9
Dual homing for Access nodes (like OLTs)
In Service Software Upgrades (ISSU)
In-band control for remote switches
Scale & Performance improvements
Netconf support for port-mirroring, PTP, MACsec configuration
RBAC, AAA
More Troubleshooting tools
Trellis Roadmap

## Slide 10
Trellis is designed for Service Providers & NFV
SDN == simpler/easier/optimized features
SDN + Programmable pipelines (P4) == New PNFs in Hw
Open-source == SP ownership & customizability
Why Trellis?

## Slide 11
Traditional Residential Access
Residence
Central Office
CPE
ONU
OLT
ETH AGG
BNG
Backbone
Network
CPE – Customer Premises Equipment
OLT – Optical Line Termination
BNG – Broadband Network Gateway

## Slide 12: OLT Disaggregation
ONOS
vOLT Agent
OpenFlow Agent
OpenFlow
VLANs
GPON OLT MAC (Celestica)
AAA
Mcast
GPON OLT
NetConf
NetConf
OLT API
OMCI Stack
…
PON MAC blades
Compute blades
Backplane
VLANs, IGMP, 802.1x, Mcast …

## Slide 13
VOLTHA Overview

## Slide 14: VOLTHA Current Features (v1.3)
Microservices architecture (in progress) - VOLTHA is a set of containers
  Northbound interfaces OF, Netconf and Rest are separate containers
  VOLTHA Core is a separate container (though not a microservice)
High Availability cluster of VOLTHA instances
Supports XGS-PON and GPON networks
  Supports a number of vendor OLT & ONU adaptors from Ciena, Radisys, Nokia, Adtran, Tibit and Calix.
  Supports 2 whitebox OLTs from EdgeCore (XGS-PON) and Celestica (GPON)
Supports BBF yang models via XPON CLI/Rest commands for low level config

## Slide 15: Voltha Core 2.0 – 4 µservices
NorthBound Affinity Routing Proxy
SouthBound Affinity Routing Proxies
Handles device-specific operations:
Create/Update/delete only
Packet-out operations (OF)
Packet-in operations (OF)
Device lifecycle management (discovery -> deletion)
Device Handler µservice
Manages technology specific details (e.g xPON):
Provisioning profiles
Specialized flow decomposition
Technology Profiles µservice
Adapter X
OFAgent
REST
CLI
Netconf
Adapter Y
Adapter Sim
Adapter Test
Etcd
Etcd
Kafka
Handles:
  Read
  List
View Only µservice
Handles cluster specific operations:
event filter
backup & restore
etc.
Cluster Management µservice

## Slide 16: Industry’s First White-Box XGS-PON OLT
White-Box = Open-Hardware Specs (OCP)
+ Open-source software (ONF)
Edgecore
ASFvOLT16
Whitebox OLT
Hardware available
July 2017
VOLTHA
core
Whitebox OLT
(including EdgeCore)
OpenOLT Adaptor
GRPC
generic
protobufs
C++ GRPC srv
Py GRPC client
Chip Driver
SDK(s)
OpenOLT Software

## Slide 17: Abstraction: PON as a Quasi-Ethernet Switch
Match
Action
Meter
Queues
Scheduler
In-port
pbits
Push vlans
Apply meter
Assign queue
Outport
UNI
Ports
NNI
Ports
Match
Action
Meter
In-port
Push vlans
Apply meter
GOTO table
Outport
NNI
Ports
Table
Pbit mapping
Queuing policy (GEM)
TCONTs (BW)
GEMs per TCONT
Scheduler policy
UNI
Ports
Technology Profiles

## Slide 18: VOLTHA Trials
VOLTHA 2.0 is targeted for trials at - AT&T, Deutsche Telekom, Telefonica, GFiber
Interest from many others –
  Turk Telecom
  British Telecom
  Telecom Italia
  FastWeb
  Portugal Telecom
CenturyLink
Comcast
NTT
Reliance Jio
China Mobile

## Slide 19
Traditional Residential Access
Residence
Central Office
CPE
ONU
OLT
ETH AGG
BNG
Backbone
Network
CPE – Customer Premises Equipment
OLT – Optical Line Termination
BNG – Broadband Network Gateway

## Slide 20
Residential CORD – Disaggregated Services
Residence
Central Office
CPE
ONU
OLT
Backbone
Network
vBNG
VOLTHA
Quagga
BNG
ETH AGG
Virtual OLT
manages and abstracts PON
VNF/PNF for per
Subscriber policies
Routing control protocols
(BGP, OSPF) for interfacing
with upstream network
Fabric provides vRouter
Forwarding plane
& network functions replacing the
ETH AGG and BNG
Trellis Fabric
+ the ability to introduce other edge-compute services per subscriber

## Slide 21
Broadband
World Forum (BBWF)
Berlin, Oct’17

## Slide 22
VOLTHA
ONOS Cluster
vOLT
dhcp
mcast
OF
TP
TP
TP
NNI
OLT
ONU
UNI
Compute
Fault mgmt
Config
Accounting
Performance
Security
Inventory
BNG as a
workload option
External physical BNG
vBNG in compute
BNG as PNF in Agg switches
BNG as PNF in OLT boxes
AGG
AGG
SR
FPM
T3
OF/P4
new R-CORD
Network Edge Mediator (NEM)
REST
Kafka
Redfish
OpenStack Nova
K8
Redfish
GF backend
ONAP
Legacy OSS
OSAM-Local
EMS/NMS-adaptor
OSAM-Central
Peripheral/PNF/Pod
All control software deployed as Docker containers on compute nodes using Kubernetes
Subscriber traffic
‘fast-path’ to Internet. Redirected to compute for additional services.

## Slide 23: Thank you!
and more…