## Slide 1: SEBA: SDN Enabled Broadband Access Saurav Das Director of Engineering, ONF
October 25, 2018

## Slide 2: The ONF Ecosystem – 160+ Members Strong
70+
70+
Vibrant Operator Led Consortium Positioned for Success
Operator Partners
Vendor Partners
Innovator Operators
Innovator Vendors
Collaborators
Guru Parulkar, Exec Dir
Andre Feutsch - CTO
Jochen Appel - VP
Amin Vahdat - Fellow
Dai Kashiwa - Director
Rob Howald - VP
Shao Guanglu - SVP
Patric Lopez - VP
Firat Yaman Er - CSO
Nick McKeown - Prof
CHAIR:
ONF BOARD
Notes: The other most important thing about ONF is that we are an operator led organization.
We are by the operator and for the operator.
Our board members are leaders from leading network operators.
We appreciate Turk Telekom as a partner.
We also include 15 other network operators as members and here we appreciate Turk Cell as our member.
We do have supply-chain partners and a very strong ecosystem.

## Slide 3: CORD: Central Office Re-Architected as a Datacenter
Access Service Orchestration & Control
Mobile vBBU. vMME, vSGW, vPGW, vCDN
ROADM (Core)
BBUs
PON OLTs
Residential vOLT, vSG, vRouter, vCDN
Enterprise vCarrierEthernet, vOAM, vWanEx, vIDS
COTS (Off-the-Shelf) x86 Compute
White-box Switches with
Merchant Silicon
Economies of a datacenter, Agility of a cloud provider
SDN
NFV
Cloud

## Slide 4: SEBA Exemplar (built on CORD platform)
Mobile
ROADM (Core)
Radio Units
PON OLTs
PON OLTs
Residential
Enterprise
Shared Cloud Infrastructure
Residential Services
Mobile Services
Enterprise Services
SEBA
VOLTHA
ODTN
Stratum
ORAN
Trellis
ONOS
NEM Network Edge Mediator OSS mediation & FCAPS support for operationalization Leverages XOS project & toolchain

## Slide 5: Outline
VOLTHA – Disaggregated Residential Access
Trellis – Multi-purpose Leaf-Spine Fabric
CORD platform – service delivery at the edge
SEBA Exemplar Implementation
SEBA development & roadmap

## Slide 6: VOLTHA: Disaggregated Residential Access

## Slide 7
Traditional Residential Access
Residence
Central Office
RG
ONU
OLT
ETH AGG
BNG
Backbone
Network
RG – Residential Gateway
OLT – Optical Line Termination
BNG – Broadband Network Gateway

## Slide 8
Disaggregated Residential Access
Residence
Central Office
RG
ONU
OLT
Backbone
Network
VOLTHA
BNG
ETH AGG
Virtual OLT
manages and abstracts PON
vBNG
VLAN termination,
Hierarchical QoS
DHCP
Fabric provides
Eth aggregation
Routing
Leaf-Spine Fabric
+ the ability to introduce other edge-compute services per subscriber
vBNG
OLT MAC
AAA

## Slide 9: OLT Disaggregation  VOLTHA
ONOS
VOLTHA
OpenFlow Agent
OpenFlow
VLANs
GPON OLT MAC (Celestica)
AAA
Mcast
GPON OLT
NetConf
NetConf
OLT API
OMCI Stack
…
PON MAC blades
Compute blades
Backplane
VLANs, IGMP, 802.1x, Mcast …
VOLTHA: Virtual OLT Hardware Abstraction

## Slide 10: VOLTHA Operation
ONOS
VOLTHA
OLT
ONU
NNI
UNI
UNI
Logical
switch
Switch
VLANs
dhcp
mcast
Bridging/Routing

## Slide 11
VOLTHA Architecture

## Slide 12: Industry’s First White-Box XGS-PON OLT
White-Box = Open-Hardware Specs (OCP)
+ Open-source software (ONF+OCP)
Edgecore
ASFvOLT16
Whitebox OLT
Available
July 2017
VOLTHA
core
Whitebox OLT
(including EdgeCore)
OpenOLT Adaptor
GRPC
generic
protobufs
C++ GRPC srv
Py GRPC client
Chip Driver
SDK(s)
OpenOLT Software

## Slide 13: Why OpenOLT Adaptor?
Generic OLT adaptor - ease of onboarding for new vendors (including whitebox vendors)
VOLTHA
core
Whitebox OLT
(including EdgeCore)
OpenOLT Adaptor
GRPC
(generic
protobufs)
March 2018
C++ GRPC srv
Py GRPC client
Chip Driver
SDK(s)
VOLTHA CORE
OpenOLT
EdgeCore OLT
Iskratel
OLT
OpenOMCI ONU
CIG
OLT
Alpha ONU
Iskratel ONU
Arcadyan ONU
CIG ONU
Tellabs ONU
Tellabs
OLT

## Slide 14: Trellis: Multi-purpose leaf-spine fabric

## Slide 15
Multi-purpose leaf-spine
fabric designed for NFV
Bare-metal hardware
Open-source software
SDN-based (built on ONOS)
Trellis Overview

## Slide 16
Bridging with Access & Trunk VLANs (within a rack)
Routing (inter-rack)
  IPv4 & IPv6 Unicast routing with MPLS Segment-Routing
  IPv4 & IPv6 Multicast routing
Dual-homing for compute-nodes and external routers
Multi-stage fabrics (2 layers of spines)
vRouter - entire fabric behaves as a single router
  BGP (v4/v6) support for external (upstream) connectivity
  Static routes, route blackholing
  DHCP L3 relay (IPv4/v6)
MPLS Pseudowires
QinQ termination
T3 - Trellis Troubleshooting Tool
ASIC Support
  Broadcom Qumran, Tomahawk, Trident2 switches from EdgeCore & QCT
  Preliminary support for Cavium Xpliant switches and P4-based Tofino switches
Trellis Features

## Slide 17
White Box Switch
EdgeCore 5712,5912
QCT LY8
Leaf Switch
48 x 10G, 6 x 40G/100G
GE mgmt.
White Box Switch
EdgeCore 6712,7712
Spine Switch
32 x 40G/100G ports downlink to leaf switches
GE mgmt.
BRCM ASIC
OF-DPA
Indigo OF Agent
OpenFlow 1.3
OCP: Open Compute Project
ONL: Open Network Linux
ONIE: Open Network Install Environment
BRCM: Broadcom Merchant Silicon ASICs
OF-DPA: OpenFlow Datapath Abstraction
Leaf/Spine Switch Software Stack
to controller
OCP
Software
(ONL,ONIE)
OCP Bare Metal Hardware
White-Box = Bare-metal hw + Open-Source sw
Trident2, Tomahawk, Qumran

## Slide 18
Ingress
Port Table
Phy Port
Vlan Table
Termin-ation MAC
Table
Multi-
cast Routing Table
Unicast
Routing
Table
MPLS
Table
Bridging
Table
ACL
Policy
Table
L2 Flood
Group
L3 ECMP
Group
Phy Port
Phy Port
Phy Port
Phy Port
Phy Port
MPLS
Label
Group
MPLS
Label
Group
L3
Mcast
Group
L2 Interface
Group
L2 Interface
Group
Fabric ASIC Pipeline* (BRCM’s OF-DPA)
Vlan 1 Table
MPLSL2 Port
Table
* Simplified view
Abstracts underlying ASIC
Enables programming of all
flow-tables & port-groups
Why OF-DPA?
L2 Interface
Group
Phy Port
L2 Interface
Group
Notes: Talk about data plane scale

## Slide 19
ONOS Cluster
P4Runtime
gNMI
Barefoot Tofino
Mellanox
Cavium Xpliant
fabric.p4 driver
Trellis & P4
OF-DPA driver
Brcm Qumran
Brcm Trident2
Brcm Tomahawk
OpenFlow
NetConf
Segment Routing
DHCP L3 Relay
vRouter
Multicast
SPGW-app
Same set of Trellis applications on ONOS
P4
capable hardware
Allowing new functionality on hardware (demo at MWC ‘18)
P4
Enhanced with P4 program deployment and pipeline configuration

## Slide 20: CORD Platform: service delivery @ the edge

## Slide 21: New CORD 6.0 platform (July-2018)
Bare metal server
Bare metal server
Bare metal server
OS
OS
OS
Management network
ONOS
XOS
Kafka
Leaf
Leaf
Spine
Spine
Access
Node
Upstream
Dataplane network
OS
OS
OS
OS
OS
CORD control software  set of Docker containers deployed on Kubernetes using standard tools like Helm charts
profile
Kubernetes
ELK
Grafana
Prometheus
Notes: No distinction between head-node and compute node
Offline install – local docker registry
Modularity - install what you need – choose helm chart, your own fabric, your own DNS
1 switch/ 1 server – expand as you wish

## Slide 22: SEBA – A profile loaded on the CORD platform
Bare metal server
Bare metal server
Bare metal server
OS
OS
OS
Management network
ONOS
XOS
Kafka
Leaf
Leaf
Spine
Spine
Access
Node
Upstream
Dataplane network
OS
OS
OS
OS
OS
CORD control software  set of Docker containers deployed on Kubernetes using standard tools like Helm charts
profile
Kubernetes
ELK
Grafana
Prometheus
VOLTHA
workflow
onos apps
Runtime config & service instantiation
Notes: No distinction between head-node and compute node
Offline install – local docker registry
Modularity - install what you need – choose helm chart, your own fabric, your own DNS
1 switch/ 1 server – expand as you wish

## Slide 23: SEBA Exemplar Implementation

## Slide 24: SEBA Exemplar
VOLTHA
ONOS Cluster
vOLT
dhcp
mcast
OF
TP
TP
TP
NNI
OLT
ONU
UNI
Compute
AGG Switch
AGG Switch
SR
FPM
T3
OF
Network Edge Mediator (NEM)
Redfish
Redfish
ONAP
Legacy OSS
OSAM-Local
EMS/NMS-adaptor
OSAM-Central
SEBA POD
All control software deployed as containers on compute nodes using Kubernetes
Subscriber traffic
‘fast-path’ to Internet
Providing FCAPS & Inventory
REST
Kafka
Built on the new CORD platform

## Slide 25: NEM Workflows
VOLTHA
ONOS Cluster
vOLT
dhcp
mcast
OF
TP
TP
TP
NNI
OLT
ONU
UNI
Compute
AGG Switch
AGG Switch
SR
FPM
T3
OF
Network Edge Mediator (NEM)
Redfish
Redfish
SEBA POD
All control software deployed as containers on compute nodes using Kubernetes
Subscriber traffic
‘fast-path’ to Internet
BNG is a workload option
External physical BNG
vBNG in compute
BNG in Agg switches
BNG in OLT boxes
Providing FCAPS & Inventory

## Slide 26
RG
VOLTHA
ONOS
TP
TP
TP
NNI
OLT
ONU
UNI
Compute
AGG
BNG
NEM
KAFKA
PROMETHEUS
ELK STACK
GRAFANA
KIBANA
XOS
Operator OSS
NEM Monitoring
Infrastructure
Alarms, events & stats
Logs

## Slide 27
Demo setup BBWF 2018
ONF Booth (Hall 22a, Booth B116)
NEM User Interface: runtime service instantiation, inventory, workflow status
NEM Monitoring Dashboard: stats, events, logs (FCAPS)

## Slide 28: Demo setup BBWF 2018
VOLTHA
ONOS
vOLT
dhcp
aaa
EdgeCore OLT
ONU
Compute
Nodes
EdgeCore AGG Switch
SR
SEBA Peripheral/PNF/Pod
RG
BNG
DHCP Server (subscriber RG addressing)
Public Internet
Radius Server
Configuration
Grafana/Kibana
Prometheus
Kafka
XOS GUI
Exporter
XOS Core
Chameleon
Synchronizers
Tosca
Database
Network Edge
Mediator (NEM)
Elasticsearch
Logstash
sadis
kafka-i
Iskratel OLT (X)
CIG OLT
Adtran OLT
Iskratel OLT (G)
Alpha
RG
Iskratel
RG
Arcadyan
RG
Adtran
RG
CIG
RG
RG
Iskratel
Iskratel
BBSim
Software Stack
Hardware

## Slide 29
Demo setup BBWF 2018
ONF Booth (Hall 22a, Booth B116)
OLTs: Adtran, CIG,
EdgeCore & Iskratel
Servers: VOLTHA, ONOS, XOS, K8s, ELK, Docker, Prometheus, Grafana, Kibana
ONUs: Arcadyan, Alpha, Adtran, CIG, Iskratel
AGG switch: EdgeCore

## Slide 30: SEBA Development & Roadmap

## Slide 31
Distributed DevOps - SEBA
SEBA System
End-to-End
OLT, Switch
Hardware
Redfish APIs
OLT
Software (BAL)
AT&T
OpenOMCI
OLT & ONU
VOLTHA 2.0
VOLTHA 2.0
Technology Profiles
Test automation
Certification
Simulator

## Slide 32
SEBA Distributed DevOps – ONF Responsibilities
Daily scrum
Bugs - issue analysis; root-cause;
Design discussions for new features
Documentation
Recommend best-practices/training
Joint Development
with AT&T Foundry
Support
VOLTHA/SEBA Community
Weekly SEBA public meetings
JIRA issues – kanban methodology
Mailing lists, Slack community support
VOLTHA meetings, TST, architectural guidance
Deliver
New
Features
ONF team resposible for all ONOS and NEM feature development
FCAPS features – kpis, alarms & logs in SEBA monitoring infrastructure
AT&T workflow development
Integrate with new ONU and OLT vendors
AGG switch features
SEBA/VOLTHA Stability & Scale
Focus on stability of VOLTHA – robustness and repeatability
Investigate scalability and performance of full SEBA system
Tooling
BBSim – Guide NTT in the development of PON simulator
SEBA-in-a-BOX: Complete end to end emulation of SEBA system with ponsim & mininet
QA
Developing automated feature tests
Extending framework for hardware based end-to-end tests
Work with community to develop test automation and certification procedures

## Slide 33
Internal GE Management Switch
SEBA POD
EdgeCore OLT
EdgeCore OLT
EdgeCore OLT
EdgeCore OLT
Up to 16
OLT devices
AGG Switch
(Tomahawk
32 x 100G)
AT&T
External BNG
Compute Node
Compute Node
Compute Node
VOLTHA, ONOS, NEM, Kubernetes, Docker registry,
Gateway VM
Abstract OLT
ONU+RG
ONU+RG
ONU+RG
Up to 64 ONUs per PON port
Up to 16 PON ports / OLT device
DHCP Server (subscriber RG addressing)
DHCP Server (POD addressing)
Radius Server
External OSS
Public Internet
SEBA Deployment Goal @ AT&T

## Slide 34
Roadmap
BNG Disaggregation
Using P4 in Aggregation switch
Implementing more operator workflows
Performance & scale improvements for Trials
Redundancy
Integrating VOLTHA 2.0 & Technology profiles
ISSU
Integrating M-CORD profile to use SEBA as mobile backhaul

## Slide 35
Summary
ONF: Operator driven curated open source
  CORD is the flagship umbrella project
  SEBA exemplar implementation is built on the CORD platform
Components:
  VOLTHA abstracts the PON as a quasi-Ethernet switch to the SDN controller
  Trellis manages a multi-purpose leaf-spine fabric
  VOLTHA and Trellis compatible white-box OCP hardware
  CORD: service delivery platform - set of Docker containers managed by K8s
SEBA: SDN Enabled Broadband Access
  SEBA – a profile instantiated on CORD, jointly developed by ONF, AT&T & community
  NEM – northbound interfaces for integration with operator backends
  Significant focus on FCAPS infrastructure
  Multiple operator workflows
  Headed to trials at AT&T, significant interest from operators worldwide