## Slide 1: State of ONF Saurav Das, Guru Parulkar, Oğuz Sunay, ONF

## Slide 2: ONF’s Operator Led Mission
Disaggregation White Box
Open Source
SDN/NFV/ Cloudification
… to bring capex & opex efficiencies & innovative services
Transform Operator Networks
by leveraging
Why?
How?
With the focus on Access and Edge
Notes: ONF is an operator led industry consortium. I will explain later why and what it means.
And our mission is to transform operator networks and to bring Capex and Opex efficiencies and enable operators to create innovative revenue generating services.
And we achieve our goals by leveraging or building on the architecture innovations such as SDN, NFV and Cloudification as well as Disaggregation and Open Source.
What is important to note is that we are not just about open source or just about SDN or NFV.
We believe if we have to achieve the transformation we all seek, we have to work with and emphasize all these together and that is only way we can succeed with our mission.
And we are very mission oriented in this pursuit.
You can contrast this with other communities that simply focus on open source or bringing developers together without a clear shared mission.

## Slide 3: ONF Unique Approach – Operator Led Curated Open Source
  “Small & mighty” independent engineering team
  Dedicated to the mission with no legacy to protect
Lab & Engineering Staff @ ONF
Operator Partnerships 7+ Years
Operator prioritized use cases
  Operators first agree on common Use Cases to jointly pursue
  Operators commit to deployment
Keiretsu Ecosystem Develops
  Curated supply chain engages to embrace opportunity
  Well aligned vendors each contribute value to overall solution
  Operator commitment to deployment ensures ROI
Notes: So let me explain how our curated open source model and community work.
Consider network operators such as AT&T, Comcast, China Unicom, DT, Google, NTT and Turk Telekom.. They own and operate largest infrastructure and services. And they are committed to transforming their networks and they know the best their priorities and how they want to approach it.
These operators specify and help define the use cases and solutions they want to pursue and commit to deployment.
Then we have a small engineering team of 20-25 architect and developers that some times our board members describe as “small and mighty ” – because we don’t have any legacy to protect and we pursue innovative architecture and solutions with a passion. On many occasions, industry folks have said we are crazy or pursuing things that will not work and our team has proven them wrong.
Then we have a list of supply-chain partners who are committed to this vision/mission of creating SDN and NFV with disaggregation and open source. These supply-chain partners get to work closely with operators on platforms and solutions they want deploy. Thus these supply-chain partners don’t have to do guess work and can significantly cut their R&D costs and reduce time to market.
And together we have created some amazing open source platforms and solutions – I will talk about them in just a minute.

## Slide 4: Operator Led - Curated Open Source Community
Partners committed to disaggregation, open source and SDN/NFV/Cloudification

## Slide 5: Highlights
All pieces coming together for wireline and mobile access and edge
Key platforms and solution proven in a tier-1 production setting
  Trellis: ONOS and leaf-spine fabric with ”real” SDN and white boxes
Other platforms and solutions proven and quickly moving to production readiness
  SEBA: VOLTHA, ONOS, NEM (AT&T, DT, TT, …)
  OMEC: Open source CUPS compliant EPC (DT, Sprint)
  SD-RAN and Mobile Edge Cloud (China Unicom)
Exciting forward looking roadmap
  Next Gen SDN offering: top-down programming, zero-touch operation, network verification, fine-grained measurement, closed loop control
  COMAC: convergence of access and core
Notes:   Overall ONF mission
  Specific platforms and solutions
  Deployments

## Slide 6: Transforming Wireline and Mobile Access and Edge
SDN Control Plane: ONOS
White boxes: Servers, Switches, OLT, RAN
Access and Edge Network Substrate: Trellis Fabric
Wireline
Access
Wireline Core: BNG
VOLTHA
SD-BNG
Mobile
RAN
Mobile Core: EPC
SD-RAN
OMEC
SEBA

## Slide 7: Production-ready Multi-purpose leaf-spine fabric
Leaf
Leaf
Spine
Spine
Central Office
Leaf
Leaf
Trellis apps
IPv4/v6 unicast/multicast, vlans, MPLS SR, vRouter …
ONOS Cluster
Internet
Metro/Core
Routers
Base station
R-PHY
R-OLT
Leaf
Leaf
SDN-based
White-boxes
Open-source
Tenets
1
Types of Traffic
Optimized for Service Provider Access/Edge
2
Types of Switches

## Slide 8: Production-ready Multi-purpose leaf-spine fabric
Leaf
Leaf
Spine
Spine
Central
Office
Leaf
Leaf
Trellis apps
IPv4/v6 unicast/multicast, vlans, MPLS SR, vRouter …
ONOS Cluster
Internet
Metro/Core
Routers
Leaf
Spine
Spine
Leaf
Field Office
Base station
R-PHY
R-OLT
Optimized for Service Provider Access/Edge
3
Distributed
Fabric
Notes: USE CASE 1 – Distributed Fabric for Access/Edge Networking

## Slide 9
Learn more about Trellis – Friday
George Tchaparian
President & CEO
EdgeCore Networks
Saurav Das
VP Engineering
ONF
Nitesh Bansal
SVP & Global Head Engineering Services
Infosys

## Slide 10: Transforming Wireline and Mobile Access and Edge
SDN Control Plane: ONOS
White boxes: Servers, Switches, OLT, RAN
Access and Edge Network Substrate: Trellis Fabric
Wireline
Access
Wireline Core: BNG
VOLTHA
SD-BNG
Mobile
RAN
Mobile Core: EPC
SD-RAN
OMEC
SEBA

## Slide 11
Traditional Wireline Access
Residence
Central Office
RG
ONU
OLT
ETH AGG
BNG
Backbone
Network
RG – Residential Gateway
OLT – Optical Line Termination
BNG – Broadband Network Gateway
Each device closed, proprietary, and not programmable
Source of high capex and opex for operators
Opportunity to bring SDN, disaggregation, and open source as operators deploy next gen broadband with GPON, XGS-PON, G.Fast, …

## Slide 12
Residence
Central Office
RG
ONU
OLT
ETH AGG
BNG
Backbone
Network
RG – Residential Gateway
OLT – Optical Line Termination
BNG – Broadband Network Gateway
VOLTHA
Virtual OLT
manages and abstracts PON
OLT MAC
WhiteBox
Switch
Trellis
Manages 1 or more switches
SEBA: SDN Enabled Broadband Access

## Slide 13
VOLTHA apps
VOLTHA
SDN Controller - ONOS
Network Edge Mediator (NEM)
SEBA POD
Trellis apps
ONAP
Op X OSS/BSS
Local Adaptor
DockerK8s Helm
OLT
ONU
External BNG
SWITCH
SERVER
SEBA: SDN Enabled Broadband Access

## Slide 14
SEBA 1.0 (Jan 7th 2019)
HSIA service
AT&T workflow
VOLTHA 1.6
New CORD platform (6.1)
SEBA 2.0 alpha (July 3rd 2019)
Technology & Speed Profile
AT&T workflow, HSIA service
VOLTHA 1.7, BAL 2.6
SEBA 2.1 (Sept/Oct 2019)
BAL 3.1
SEBA 3.0 & Beyond
VOLTHA 2.x
Embedded BNG
DT/TT Workflows
SEBA Update
ONF operators AT&T, DT, and TT are committed to taking SEBA to production

## Slide 15
Residence
Central Office
RG
ONU
OLT
ETH AGG
BNG
Backbone
Network
RG – Residential Gateway
OLT – Optical Line Termination
BNG – Broadband Network Gateway
VOLTHA
Virtual OLT
manages and abstracts PON
WhiteBox
Switch
OLT MAC
Trellis
Manages 1 or more switches
Many functions (Closed Integrated Device):
Subscriber tunnel termination (QinQ, PPPoe)
Accounting
Hierarchical QoS
Lawful intercept (wiretap)
Wholesale tunnel relay (e.g. L2TP)
Multicast
Routing
SEBA: SDN Enabled Broadband Access

## Slide 16
Residence
Central Office
RG
ONU
OLT
ETH AGG
BNG
Backbone
Network
RG – Residential Gateway
OLT – Optical Line Termination
BNG – Broadband Network Gateway
VOLTHA
Virtual OLT
manages and abstracts PON
OLT MAC
P4 based WhiteBox
Switch with BNG-user plane
Trellis
Manages 1 or more switches
SEBA with SD-BNG
BNG-c
SD-BNG

## Slide 17
VOLTHA apps
VOLTHA
SDN Controller - ONOS
Network Edge Mediator (NEM)
SEBA POD
Trellis apps
Docker K8s Helm
OLT
ONU
Embedded BNG
P4-SWITCH
SERVERS
BNG-control
P4Runtime, gNMI, gNOI
STRATUM
Upstream Routers
ONU
STRATUM
SEBA with SD-BNG
1
BNG-c app on ONOS
PPPoE server
1
Integrate existing control software
2
BNG-u
Func distribution
Notes: Our plan is to split the BNG black box in two pieces, user plane and control plane
The control plane, responsible of functions like authentication, IP address assignment, routing, etc. can be implemented as a mix of SDN apps running on top of ONOS, integrated with existing control software when possible
The user plane, responsible of processing data traffic, can be implemented as part of the existing fabric of SEBA, using P4 and merchant silicon. We plan to use different chipsets for disfferent fiunctions

## Slide 18: SD-BNG Integration with SEBA Demo at ONF Connect
OLT
Switch (P4)
Upstream router
ONOS
Trellis
BNG-c Relay
Stratum
ONU
SEBA Apps
VOLTHA
NEM
Kubernetes cluster (compute node)
PPPoE Server
Subscriber with PPPoE client
Internet
Handles authentication, address assignment (IPCP), keep-alive, etc.
Notes: Traditional SEBA deployment augmented with new components:
Subscriber device configured to act as a PPPoE client
External PPPoE server
BNG-c Relay app

## Slide 19: Transforming Wireline and Mobile Access and Edge
SDN Control Plane: ONOS
White boxes: Servers, Switches, OLT, RAN
Access and Edge Network Substrate: Trellis Fabric
Wireline
Access
Wireline Core: BNG
VOLTHA
SD-BNG
Mobile
RAN
Mobile Core: EPC
SD-RAN
OMEC
SEBA

## Slide 20: Mobile Network Evolution Towards 5G
Telco Cloud
DISAGGREGATED, CUPS
3GPP CORE VNFS
IMS
APPS
UEs
Public
Cloud
eNB/gNB
eNB/gNB
UEs
eNB/gNB
3GPP
RAN STACK
UEs
OTT APPS

## Slide 21: Mobile Network Evolution Towards 5G
Telco Cloud
Pieces Coming Together
eNB/gNB
DISAGGREGATED, CUPS
3GPP CORE VNFS
Edge
Edge
CU
CU
3GPP CORE
APPS
OTT APPS
SDN CONTROL
Public
Cloud
OTT APPS
UEs
eNB/gNB
UEs
eNB/gNB
UEs
3GPP
RAN STACK
RU
DU
DU
DU
RU
RU
1
2
3
OMEC: Open Source
Disaggregated Mobile Core
Mobile Edge Cloud Platform
with Hybrid Cloud Connectivity
SD-RAN: Near Real-Time
Control of RAN with ONOS
IMS
APPS

## Slide 22: RAN Evolution: Towards SD-RAN
SD-RAN Controller can also control non-disaggregated eNBs/gNBs
DISAGGREGATION
+
SD-CONTROL
RRC
PDCP
RLC
MAC
PHY
Scheduling
DISAGGREGATION
RU
DU
PHY-LO
PHY-HI
MAC
RLC
CU
PDCP
RRC
Scheduling
CU-C
CU-U
ONOS SD-RAN
(O-RAN RIC)
PDCP-U
SDAP
PDCP-U
RRC
E1
E2
E2
E2
E1 & E2 to be specified by O-RAN
Demo to use an interim E2 interface inspired by O-RAN
Packet & Signal Processing
Radio Resource Management Control
All-In-One
eNB/gNB
E2

## Slide 23: ONOS-Based SD-RAN Controller
DISTRIBUTED RIC NEAR-RT CORE
(R-NIB management, Notifications, High-availability & Scale-out)
O-RAN COMPLIANT SB - E2
RAN APPS
(Radio Connection Mgmt, Mobility Mgmt, QoS Mgmt, Interference Mgmt, 3rd Party Apps, Trained Model)
O-RAN COMPLIANT NB - A1
INTERIM E2:
ASN.1 OVER SCTP
NB CORE API
(R-NIB, Flow Objectives, Intents)

## Slide 24: ONOS SD-RAN Features
ONOS maintaining and displaying the Mobile Network State over the entire geography
ONOS-Based SD-RAN controller supporting an interim E2 southbound
A simple handover application running on ONOS SD-RAN conducting near real-time control
A simple radio channel emulation platform distributing SD-RAN compliant base stations and mobile handsets over a geography
Can we drop this slide?

## Slide 25: ONOS SD-RAN Demo at ONF Connect
R-NIB
GUI
Handover App
6. Handover takes place. The updated mobile network state is transmitted up to ONOS SD-RAN
2. Base stations transmit time-varying mobile network state information to ONOS SD-RAN every 5ms using the interim E2 interface
1. Mobile Handsets transmit mobile channel quality info to their serving base station every 1ms following 3GPP standards
3. ONOS SD-RAN maintains and displays time-varying mobile network state in near-real-time
4. R-NIB is exposed to the RAN handover application. When necessary, this app triggers handovers
5. When handover is triggered, ONOS SD-RAN orders the serving and target base stations to execute it using E2

## Slide 26: OMEC: Pieces Moving Towards Productization
CI/CD: Automated standards compliancy testing and heavy RAN traffic performance testing
HSS
MME
Subscriber
Database
PCRF
PGW-C
SGW-C
SGW-U
PGW-U
Billing & Charging
  Architectural improvements are underway. The goal is to develop an architecture that makes it easy to migrate to: i. 5G ii. Cloud-native.
CUPS compliant SGW and PGW user and control planes have been hardened towards production deployments

## Slide 27: OMEC Field Trials
Operator: T-Mobile Poland
Use Case: Fixed-Mobile Substitution
Trial with Live Customers
Beginning: August/September 2019
Operator: Sprint USA
Use Case: Local Break-Outs
Field Trials
By: End of 2019

## Slide 28: OMEC Gateways Perform at Scale (Demo at ONF Connect)
Showcasing OMEC can securely run on high volume servers and deliver operational capacity
Capacity  13+ VNFs  100 Cores 256GB 1TB HDD 8x10GbE  250K Flows / 1000TPS / 2MPPS

## Slide 29: Mobile Edge Cloud with Hybrid Cloud Connectivity
RU+DU
+CU-U
SDN
FABRIC
MOBILE
EDGE CLOUD
SANTA CLARA
MENLO PARK
VPN
INTERNET

## Slide 30: Mobile Edge Cloud with Hybrid Cloud Connectivity
CU-RADIS
ONOS RAN
SPGW-U
SPGW-C
MME
HSS
HSS-DB
CDN-LOCAL
CDN-REMOTE
PROGRAN
ONOS
NEM
KUBERNETES
CU-NATS
CU-L3
KUBERNETES
RU+DU
+ CU-U
VPN
SDN
FABRIC
SR-IOV
SR-IOV
SR-IOV
MOBILE
EDGE CLOUD
INTERNET
SANTA CLARA
MENLO PARK
Demo at ONF Connect

## Slide 31: Mobile Edge Cloud Software Stack
Piecing SD-RAN, OMEC and Hybrid Cloud Connectivity Together
Multi-Access Edge Cloud Stack
INTERFACES
Telco Central Cloud
Inter-Cloud Connectivity
Inter-Cloud
Connectivity
Edge State Data
Mobile Edge Cloud Profile
PROFILES
NEM
Kubernetes
ONOS
ONOS SD-RAN
RAN Apps
Trellis
RAN VNFs
Apps
Apps
Core VNFs
Core VNFs

## Slide 32: ONF’s First Official Mobile Edge Cloud Release
Graduating from Demo Quality To Field Trial Quality Towards Production Readiness
ONOS
Trellis Apps
Kubernetes
NEM
Prometheus / Grafana
Leverages the latest SEBA platform which is
hardened for deployment
OMEC
RAN Apps*
ONOS
SD-RAN*
Mobile Subscriber State
SD-RAN controller is based on ONOS which has been hardened for Trellis
Further development will be in synch with μONOS processes
RAN Apps development will follow the same processes that other ONF projects use
Mobile subscriber state for FCAPS is OMEC based and
uses OMEC processes for dev
M-CORD has conducted very successful demonstrations
Focus has been on showcasing cutting-edge technology
ONF Mobile Edge Cloud Platform
Official Release Date:
September 20, 2019
OMEC dev follows the same processes that other ONF projects use
Gateway components hardened for deployment
MME component is being enhanced towards deployment
China Unicom will use this platform in its field trials for SD-RAN and MAEC
* Will not be part of v1.0 release, but subsequent releases

## Slide 33: Mobile Edge Cloud Features
OMEC: Production grade, open source, CUPS compliant 3GPP core with SR-IOV accelerated user plane
Multi-Cloud Connectivity Supporting Distributed
OMEC VNFs
COMAC-EP V1.0 Release Platform: Mobile Edge Cloud with SDN-Programmable Access
OTT Services Support allowing for multi-cloud distribution of service components
COMAC Dev-as-a-Service: COMAC pod running on public cloud and capable of running E2E tests
Real-Time Monitoring of Mobile Edge State, including infrastructure state, fabric traffic, container traffic and mobile subscriber state

## Slide 34: Journey to Next-Gen SDN
Time
Value
Bold SDN vision established
Separation of Ctrl & Dataplane
Centralized Control
OpenFlow
Vendors responded with software configuration tools:
Traditional switching & routing using conventional embedded control protocols
SDN- -
Google SDN implementation
SDN
Open Source SDN Enters Production
Taking a leap forward
Top-Down Programmability
Hardware Independence
Cloud-like lifecycle
Verifiability
Next-Gen SDN
New Technologies Programmable Silicon
P4, P4Runtime
Cloud Dev Models
Lessons Learned
Enabling
Simpler forwarding devices
Faster innovation
Reduced capex/opex
Enabling
Rapid Network Innovation
Zero Touch Operation
Robust Hardware Ecosystem

## Slide 35: Nick’s Keynote

## Slide 36
Overview: Next-Gen SDN Stack
Brian O'Connor
MTS, ONF
Nate Foster
Associate Professor of Computer Science, Cornell University
Timon Sloane
VP, Marketing & Ecosystem, ONF
Thomas Vachuska
Chief ONOS Architect, ONF

## Slide 37: Stratum Going Open Source on the Following Devices
Near-term future platforms:
Additional platforms for existing targets (ONLPv2 porting)
  Existing vendors + Asterfusion, ...
Mellanox Spectrum / SN2700 via PINode and ONLPv2
Trident 2 platforms via BCM SDK6 wrapper
Datacom platforms (PowerPC-based)
Tofino
Up to 6.5 Tbps
Z9100
32 x 100 Gbps
AG9064v1
64 x 100 Gbps
Wedge100BF-32X
32 x 100 Gbps
Wedge100BF-65X
65 x 100 Gbps
Tomahawk
Up to 3.2 Tbps
D5054
32 x 100 Gbps +
48 x 25 Gbps
T7032-IX1
32 x 100 Gbps
AS7712
32 x 100 Gbps
D7032
32 x 100 Gbps
BF6064X
64 x 100 Gbps
Switching ASIC
Switch Vendor

## Slide 38: Final Takeaways
ONF and its community are on the path to transforming wireline and mobile access and edge
Our platforms are rapidly maturing and getting ready for production deployment
Our operator partners are committed more than ever