## Slide 1: SDN in the Last Mile SEBA & SD-RAN
Saurav Das
VP of Engineering, ONF
IEEE NFV-SDN Keynote
November 10th, 2020

## Slide 2: ONF: Operator Led, Curated Open Source Community

## Slide 3
ONF’s Curated Open Source Model
Notes: ONF is an operator led industry consortium.
And our mission is to transform operator networks and to bring Capex and Opex efficiencies and enable operators to create innovative revenue generating services.
And we achieve our goals by leveraging or building on the architecture innovations such as SDN, NFV and Cloudification as well as Disaggregation and Open Source.
What is important to note is that we are not just about open source or just about SDN or NFV.
We believe if we have to achieve the transformation we all seek, we have to work with and emphasize all these together and that is only way we can succeed with our mission.
And we are very mission oriented in this pursuit.
You can contrast this with other communities that simply focus on open source or bringing developers together without a clear shared mission.

## Slide 4: Agenda

## Slide 5
Traditional Broadband Access
Residence
Central Office
RG
ONU
OLT
ETH AGG
BNG
Backbone
Network
RG – Residential Gateway
OLT – Optical Line Termination
BNG – Broadband Network Gateway
ODN

## Slide 6: SEBA: SDN Enabled Broadband Access
Residence
Central Office
RG
ONU
OLT
ETH AGG
BNG
Backbone
Network
VOLTHA
Virtual OLT
manages and abstracts PON
TRELLIS
Manages 1 or more switches
Whitebox
Switch
RG – Residential Gateway
OLT – Optical Line Termination
BNG – Broadband Network Gateway
Virtual BNG
manages subscriber
services
ODN
SD-BNG
Whitebox switch with merchant silicon
OLT MAC & PHY
Notes: The goal of SEBA is that of bringing the benefits of disaggregation and open source to the case of residential access.
We do this by using SDN principles and whitebox hardware.
To make this possible we first virtualize the PON network including the OLT and the ONU using VOLTHA
We abstract all the internal complexity of the PON network and instead offer an abstraction of an OpenFlow switch
Second, we disaggregate the ethernet aggregation stage using whitebox switches and Trellis, a set of SDN apps that control a fabric of 1 or more switches
Finally, the fabric can be extended to include more advanced functions such as BNG
Let’s have a closer look at each one of these 3 componenets

## Slide 7
BNG-UP
Core
Docker
Kubernetes
Helm
Network Edge Mediator (NEM)
Edge orchestration and FCAPS micro-services
SEBA POD
ONAP
Operator OSS/BSS
Local adaptor
VOLTHA
Compute
servers
SOFTWARE STACK
HARDWARE
SDN Controller - ONOS
OpenFlow
P4Runtime,
gNMI/OpenConfig
VOLTHA apps PON/OLT control
TRELLIS apps
Fabric control
SD-BNG apps
Subscriber control
Whitebox OLT
Whitebox OLT
whitebox switch
whitebox switch
Stratum
ONU
RG
PON
SEBA
SDN
Enabled
Broadband
Access

## Slide 8
BNG-UP
Core
Docker
Kubernetes
Helm
Network Edge Mediator (NEM)
Edge orchestration and FCAPS micro-services
SEBA POD
ONAP
Operator OSS/BSS
Local adaptor
VOLTHA
Compute
servers
SOFTWARE STACK
HARDWARE
SDN Controller - ONOS
OpenFlow
P4Runtime,
gNMI/OpenConfig
VOLTHA apps PON/OLT control
TRELLIS apps
Fabric control
SD-BNG apps
Subscriber control
Whitebox OLT
Whitebox OLT
whitebox switch
whitebox switch
Stratum
ONU
RG
PON
SEBA
SDN
Enabled
Broadband
Access

## Slide 9: OLT disaggregation → VOLTHA
ONOS: SDN Controller
VOLTHA
OpenFlow Agent
OpenFlow
VLANs
AAA
Mcast
SDNize
VOLTHA Core
OLT/ONU adaptors
…
PON MAC blades
Compute blades
Backplane
VLANs, IGMP, 802.1x, Mcast …
VOLTHA: Virtual OLT Hardware Abstraction
EMS
Traditional Chassis-based Vendor OLT for PONs (Passive Optical Networks)
EdgeCore ASXvOLT16
(and others)
gRPC
On path to production in 2021
Notes: Traditional chassis-based OLT. Has PON mac blades, compute blades, backplane, management system.
Disagg -- SDNize -- OLT MACs pizza boxes, SW = Voltha manage not just the OLT but also the entire PON. Because OLT use to manage whole PON.
Because Voltha presents abstraction of PON, can run sdn controller (ONOS) on top

## Slide 10
OpenONU
VOLTHA core
Whitebox OLT
OpenOLT
Adaptor
BAL
SDK(s)
OpenOLT agent
ONL
ONIE
ONOS 1
OF Agent
Etcd
Kafka
OpenONU
Adaptor
OMCI
ONU
ONU
ONU
ONOS 1
ONOS SDN Controller
Applications
voltctl
openolt api (gRPC)
VOLTHA
stack
Bandwidth profiles
Technology
profiles
gRPC NBI
VOLTHA
Virtual
OLT
Hardware
Abstraction
Common Control & Management framework shared by all OLTs and ONUs
Hides PON level details (T-CONTS, GEM, OMCI) from the SDN controller by abstracting each PON as a simple Ethernet switch
Notes: Not independent of what comes above and below
Common c & m not just for whitebox but vendor olts as well

## Slide 11: VOLTHA Operation
ONOS
VOLTHA
OLT
ONU
NNI
UNI
UNI
Logical
switch
Switch
VLANs
dhcp
mcast
Bridging/Routing

## Slide 12
Industry’s First White-Box XGS-PON OLT
Edgecore
ASFvOLT16
Whitebox OLT
VOLTHA
core
Whitebox OLT
OpenOLT
Adaptor
Chip Driver
SDK(s)
OpenOLT Driver
ONL
ONIE
White-Box =
Open-Hardware Specs (OCP)
+ Open-Source Software (ONF & OCP)
OpenOLT

## Slide 13: Why OpenOLT Adaptor?
Generic OLT adaptor - ease of onboarding for new vendors (including whitebox vendors)
VOLTHA CORE
OpenOLT
EdgeCore OLT
Iskratel
OLT
OpenOMCI ONU
CIG
OLT
Alpha ONU
Iskratel ONU
Arcadyan ONU
CIG ONU
Tellabs ONU
Tellabs
OLT
VOLTHA
core
Whitebox OLT
OpenOLT
Adaptor
Chip Driver
SDK(s)
OpenOLT Driver
ONL
ONIE

## Slide 14: PON Management
ONOS
VOLTHA
OLT
ONU
NNI
UNI
UNI
Logical
switch
vOLT
dhcp
mcast
sadis
AAA
Kafka
Tech Profile
Speed Profile
Access Tech type
# Gems/TCONTs
Sched policy
Pbit mapping
Discard policy
Per subscriber
up/down bw profile
cir/eir/cbs/ebs

## Slide 15: SEBA Operator Workflows
AT&T workflow
TT workflow
DT FTTH workflow
DT FTTB workflow

## Slide 16
BNG-UP
Core
Docker
Kubernetes
Helm
Network Edge Mediator (NEM)
Edge orchestration and FCAPS micro-services
SEBA POD
ONAP
Operator OSS/BSS
Local adaptor
VOLTHA
Compute
servers
SOFTWARE STACK
HARDWARE
SDN Controller - ONOS
OpenFlow
P4Runtime,
gNMI/OpenConfig
VOLTHA apps PON/OLT control
TRELLIS apps
Fabric control
SD-BNG apps
Subscriber control
Whitebox OLT
Whitebox OLT
whitebox switch
whitebox switch
Stratum
ONU
RG
PON
SEBA
SDN
Enabled
Broadband
Access

## Slide 17: Fabric disaggregation → TRELLIS
ONOS: SDN Controller
Trellis Apps Bridging, vRouter, MPLS-SR, mcast, etc.
SCALE
SCALE
External router (BGP, OSPF, etc.)
OpenFlow
P4Runtime
gNMI
In production at Comcast
Carrier-grade SDN fabric for edge/NFV applications
Based on whitebox switches and merchant silicon
Leaf
Leaf
Leaf
Leaf
Spine
Spine
Leaf-Spine Fabric
With ECMP and N-way redundancy
Multi-Stage Leaf-Spine
For distributed access/edge networking
Central office
Field office
Long-haul
Extensive switch support
Vendors: EdgeCore, Delta, Inventec, Stordis, QCT
ASIC: Tomahawk, Tomahawk+, Trident2, Qumran, Tofino
Switch SW stack: ONL, OF-DPA, Stratum
Compute
Compute
Compute
Leaf (ToR)
Single Leaf
metro/ core
Access
OLT
Base station
etc.
Notes: Trellis is a set of SDN apps running on top of ONOS that provide the control plane for a carrier-grade fabric made of whitebox switches running merchant silicon
It can be used to control only 1 switch, like in this example where a top of rack / leaf is used to forward traffic between some access devices, compute servers, and an upstream router. Trellis provide a set of API that let operators enable capabilities such as bridging, routing, multicast, etc. at the network level.
Indeed, the same API and apps can be used to control a full blown leaf-spine fabric, with ECMP and N-way redundancy
...or even a multi-stage fabric where multiple leaf-spines are connected with long-haul optics
What is more, Trellis supports a number of switches from different vendors, running different ASICs and software stacks. Many of these are OCP compliant.
Open APIs such as OpenFlow, P4runtime, and gNMI are used to interact with the devices

## Slide 18: Whitebox ToR Switching
BRCM ASIC
BRCM OF-DPA
Indigo OF Agent
OCP Bare Metal Switch
SDK
ONL
ONIE
White-Box =
Open-Hardware Specs (OCP)
+ Open-Source Software (ONF & OCP)
Trellis Apps
SDN Controller
Edgecore
5712, 6712, 7712

## Slide 19
BNG-UP
Core
Docker
Kubernetes
Helm
Network Edge Mediator (NEM)
Edge orchestration and FCAPS micro-services
SEBA POD
ONAP
Operator OSS/BSS
Local adaptor
VOLTHA
Compute
servers
SOFTWARE STACK
HARDWARE
SDN Controller - ONOS
OpenFlow
P4Runtime,
gNMI/OpenConfig
VOLTHA apps PON/OLT control
TRELLIS apps
Fabric control
SD-BNG apps
Subscriber control
Whitebox OLT
Whitebox OLT
whitebox switch
whitebox switch
Stratum
ONU
RG
PON
SEBA
SDN
Enabled
Broadband
Access

## Slide 20: BNG disaggregation → SD-BNG
ONOS: SDN Controller
SDNize
Traditional Chassis-based Vendor Broadband Network Gateway (BNG)
Control Plane Apps (BNG-CP)
Authentication, address assignment, accounting, etc.
User Plane (BNG-UP)
Broadcom Qumran (DNX)
300 Gbit/s, Deep Buffers, HQoS
Intel Barefoot Tofino
3.2 Tbit/s, P4-defined routing, PPPoE term, accounting, etc.
Use merchant silicon available in fabric and OLT
OLT
FABRIC SWITCH
Specialized router:
Subscriber termination (QinQ, PPPoE)
Accounting
Hierarchical QoS
Lawful intercept
Wholesale tunnel relay (L2TP)
Multicast
Routing
Etc.
Notes: The BNG is a specialized type of router that is responsible of routing subscriber traffic to and from the operator core network. It performs many functions, such as…
Similarly to VOLTHA, we disaggregated the BNG black box in two logical pieces: the user plane and the control plane
For the user plane, which is responsible of processing subscriber data traffic, we re-use the same merchant silicon that is already available in the SEBA pod
We can use the Tofino ASIC in the fabric switch to perform functions such as routing, PPPoE termination, accounting, etc
While we can use the Qumran chip inside the OLT to perform Hierarchical QoS, since this chip is specifically designed for application that requires deep buffering
The control plane can run as an SDN apps on top of ONOS

## Slide 21
BNG CUPS API
BNG-CP → Intelligence
Choice of programming language and architecture
Provides silicon-independence & facilitates interoperability
BNG-UP → High-speed forwarding
Choice of merchant silicon and port configuration
Tofino + Qumran AX Dual-chip, HQoS in OLT (WIP)
Magenta Switch Single-chip Qumran 2C
SmartNIC Single-chip FPGA
Tofino + FPGA Dual-chip, HQoS in FPGA
FPGA
Deutsche Telekom
Dell, Intel, Benu
ONF
TU Darmstadt
Examples of HW-based implementations existing today.
Others are possible, including SW-based processing.
OLT (QAX)
Leaf switch (Tofino)
Tassen  BNG CUPS API
“Tassen: Towards a Next-Generation BNG CUPS API”
- Carmelo Cascone (ONF), Mario Kind (DT), Craig Stevens (Dell)
ONF Broadband Spotlight On-Demand Content

## Slide 22
BNG-UP
Core
Docker
Kubernetes
Helm
Network Edge Mediator (NEM)
Edge orchestration and FCAPS micro-services
SEBA POD
ONAP
Operator OSS/BSS
Local adaptor
VOLTHA
Compute
servers
SOFTWARE STACK
HARDWARE
SDN Controller - ONOS
OpenFlow
P4Runtime,
gNMI/OpenConfig
VOLTHA apps PON/OLT control
TRELLIS apps
Fabric control
SD-BNG apps
Subscriber control
Whitebox OLT
Whitebox OLT
whitebox switch
whitebox switch
Stratum
ONU
RG
PON
SEBA
SDN
Enabled
Broadband
Access

## Slide 23
SEBA Modularity
ONU
ONU
OLT
VOLTHA
AGG
switch
Compute
Nodes
ONOS
Access
apps
Fabric
apps
OS
OS
OS
K8s
NEM Orchestration (XOS)
NEM Monitoring
(Prom,Grafana, ELK)
Trellis
Kafka

## Slide 24: SEBA (and VOLTHA) Community
AT&T

## Slide 25
SEBA Surge Brigade Dashboards

## Slide 26
SEBA Surge Contributions

## Slide 27: Agenda

## Slide 28: RAN transformation: Starting point
eNB
SON
Monitoring/Logging/
Config/Control Portal
Mobile Core
BBU
RRU
Vendor Specific
Vendor Specific
Vendor Specific
S1
OSS/BSS
Vendor Specific

## Slide 29: RAN disaggregation
Step I: Horizontal disaggregation
DU
CU
Mobile Core UP
Mobile Core CP
RU
N2
N3
RRC
PDCP
RLC
MAC
PHY
Scheduling
MAC
Scheduling
RLC
PDCP
RRC
Option 7.2x
Option 2
PHY-LO
PHY-HI

## Slide 30: Joint RAN Disaggregation
Step II: Vertical disaggregation: CUPS
DU
CU
Mobile Core UP
Mobile Core CP
RU
N2
N3
CU-U
CU-C
F1-C
F1-U
N2
N3

## Slide 31: Joint RAN Disaggregation
DU
Mobile Core CP
Mobile Core CP
RU
CU-U
CU-C
F1-C
F1-U
N2
N3
Near RT Ran Intelligent Controller (nRT-RIC)
xApps
SON xApps
Policy xApps
A1
E2
E2
E2
Step III: Vertical disaggregation with SDN
RRM xApps
Non-RT-RIC
Open
Fronthaul

## Slide 32: O-RAN Architecture
DU
Mobile Core CP
Mobile Core CP
RU
CU-U
CU-C
F1-C
F1-U
N2
N3
Near RT Ran Intelligent Controller (nRT-RIC)
xApps
SON xApps
Policy xApps
A1
E2
E2
E2
RRM xApps
O1
SMO
Non-RT-RIC

## Slide 33: ONF’s SD-RAN Project  nearRT-RIC
SMO
O1 Termination
A1 Termination
E2 Termination
Subscription Mgmt
SDL
E2 Node
E2 Node
E2 Node
E2 Node
E2 Node
E2 Node
E2 Node
E2 Node
E2 Node
E2 Node
E2 Node
E2 Node
xApp
Non-RT RIC
Open APIs
nRT-RIC
Conflict Mitigation
Security
Based on
µONOS
SDN Controller

## Slide 34: Shared Goals, Shared Journey
Long Journey With Open Specifications and Open Source
O-RAN
Software Community
C-RAN
https://opennetworking.org/uncategorized/onf-commits-to-supporting-o-ran-alliance/

## Slide 35: SD-RAN Ecosystem
https://opennetworking.org/news-and-events/press-releases/onf-announces-new-5g-sd-ran-project/

## Slide 36: Summary
ONF: Operator driven curated open source
  Many projects, solutions that build on top of individual projects
  SEBA – SDN Enabled Broadband Access, built on the CORD platform
  SD-RAN – Software Defined - Radio Access Network
SEBA
  Solution integrates several other ONF projects: VOLTHA, ONOS, Trellis, SD-BNG, XOS
  Current focus areas – VOLTHA productization & SD-BNG exploration
  Production deployments in two Tier-1 operator networks in 2021
SD-RAN
  Development of O-RAN compliant, micro-ONOS based, nearRT-RIC
  Focus on new xAPPs (RRM/SON), SDKs and interoperability
Learn More
  SEBA: https://wiki.opencord.org/display/cord/seba
  SD-RAN: https://opennetworking.org/sd-ran/