## Slide 1: Telco Cloudification: From Open CORD to SDN Enabled Broadband Access (SEBA)
Saurav Das
VP of Engineering, ONF
OFC Tutorial
March 9th, 2020

## Slide 2: ONF: Operator Led, Curated Open Source Community

## Slide 3
ONF’s Operator Led Mission
Notes: ONF is an operator led industry consortium.
And our mission is to transform operator networks and to bring Capex and Opex efficiencies and enable operators to create innovative revenue generating services.
And we achieve our goals by leveraging or building on the architecture innovations such as SDN, NFV and Cloudification as well as Disaggregation and Open Source.
What is important to note is that we are not just about open source or just about SDN or NFV.
We believe if we have to achieve the transformation we all seek, we have to work with and emphasize all these together and that is only way we can succeed with our mission.
And we are very mission oriented in this pursuit.
You can contrast this with other communities that simply focus on open source or bringing developers together without a clear shared mission.

## Slide 4
Traditional Broadband Access
Residence
Central Office
RG
ONU
OLT
ETH AGG
BNG
Backbone
Network
RG – Residential Gateway
OLT – Optical Line Termination
BNG – Broadband Network Gateway
ODN

## Slide 5: SEBA: SDN Enabled Broadband Access
Residence
Central Office
RG
ONU
OLT
ETH AGG
BNG
Backbone
Network
VOLTHA
Virtual OLT
manages and abstracts PON
TRELLIS
Manages 1 or more switches
Whitebox
Switch
RG – Residential Gateway
OLT – Optical Line Termination
BNG – Broadband Network Gateway
Virtual BNG
manages subscriber
services
ODN
SD-BNG
Whitebox switch with merchant silicon
OLT MAC & PHY
Notes: The goal of SEBA is that of bringing the benefits of disaggregation and open source to the case of residential access.
We do this by using SDN principles and whitebox hardware.
To make this possible we first virtualize the PON network including the OLT and the ONU using VOLTHA
We abstract all the internal complexity of the PON network and instead offer an abstraction of an OpenFlow switch
Second, we disaggregate the ethernet aggregation stage using whitebox switches and Trellis, a set of SDN apps that control a fabric of 1 or more switches
Finally, the fabric can be extended to include more advanced functions such as BNG
Let’s have a closer look at each one of these 3 componenets

## Slide 6
AAA
VOLTHA
SDN Controller - ONOS
Network Edge Mediator (NEM)
SEBA POD
vlans
dhcp
mcast
bridging
routing
ACLs
ONAP
Op X OSS/BSS
Abstract OLT
DockerK8s Helm
OLT
ONU
External BNG
SWITCH
SERVER
SEBA
SDN
Enabled
Broadband
Access
(Embedded BNG)

## Slide 7: SEBA Components: VOLTHA

## Slide 8
AAA
VOLTHA
SDN Controller - ONOS
Network Edge Mediator (NEM)
SEBA POD
vlans
dhcp
mcast
bridging
routing
ACLs
ONAP
Op X OSS/BSS
Abstract OLT
DockerK8s Helm
OLT
ONU
External BNG
SWITCH
SERVER
SEBA
SDN
Enabled
Broadband
Access
QuantaGrid
D51B-1U
(Embedded BNG)

## Slide 9: OLT disaggregation → VOLTHA
ONOS: SDN Controller
VOLTHA
OpenFlow Agent
OpenFlow
VLANs
AAA
Mcast
SDNize
VOLTHA Core
OLT/ONU adaptors
…
PON MAC blades
Compute blades
Backplane
VLANs, IGMP, 802.1x, Mcast …
VOLTHA: Virtual OLT Hardware Abstraction
EMS
Traditional Chassis-based Vendor OLT for PONs (Passive Optical Networks)
EdgeCore ASXvOLT16
(and others)
gRPC
On path to production in 2020 at
AT&T, Deutsche Telekom, Türk Telekom
Notes: Traditional chassis-based OLT. Has PON mac blades, compute blades, backplane, management system.
Disagg -- SDNize -- OLT MACs pizza boxes, SW = Voltha manage not just the OLT but also the entire PON. Because OLT use to manage whole PON.
Because Voltha presents abstraction of PON, can run sdn controller (ONOS) on top

## Slide 10: VOLTHA Architecture
OpenONU
Adaptor
OpenONU
Adaptor
VOLTHA core
Whitebox OLT
OpenOLT
Adaptor
BAL
SDK(s)
OpenOLT driver/agent
ONL
ONIE
ONOS 1
Client
(eg. OFAgent)
Etcd
kafka
OpenONU
Adaptor
OMCI
ONU
ONU
ONU
ONOS 1
ONOS SDN Controller
Applications
VOLTHA: Virtual OLT Hardware Abstraction
Common Control & Management framework shared by all OLTs and ONUs
Hides PON level details (T-CONTS, GEM, OMCI) from the SDN controller by abstracting each PON as a simple Ethernet switch

## Slide 11: VOLTHA Operation
ONOS
VOLTHA
OLT
ONU
NNI
UNI
UNI
Logical
switch
Switch
VLANs
dhcp
mcast
Bridging/Routing

## Slide 12
Industry’s First White-Box XGS-PON OLT
Edgecore
ASFvOLT16
Whitebox OLT
VOLTHA
core
Whitebox OLT
OpenOLT
Adaptor
Chip Driver
SDK(s)
OpenOLT Driver
ONL
ONIE
White-Box =
Open-Hardware Specs (OCP)
+ Open-Source Software (ONF & OCP)
OpenOLT

## Slide 13: Why OpenOLT Adaptor?
Generic OLT adaptor - ease of onboarding for new vendors (including whitebox vendors)
VOLTHA CORE
OpenOLT
EdgeCore OLT
Iskratel
OLT
OpenOMCI ONU
CIG
OLT
Alpha ONU
Iskratel ONU
Arcadyan ONU
CIG ONU
Tellabs ONU
Tellabs
OLT
VOLTHA
core
Whitebox OLT
OpenOLT
Adaptor
Chip Driver
SDK(s)
OpenOLT Driver
ONL
ONIE

## Slide 14: PON Management
ONOS
VOLTHA
OLT
ONU
NNI
UNI
UNI
Logical
switch
vOLT
dhcp
mcast
sadis
AAA
Kafka
Tech Profile
Speed Profile
Access Tech type
# Gems/TCONTs
Sched policy
Pbit mapping
Discard policy
Per subscriber
up/down bw profile
cir/eir/cbs/ebs

## Slide 15
VLAN_0
0 → 10
UNI
3
1TCONT,
4 GEM
100.10
RG
ONU
OLT
(Stag.Ctag)
VLAN_0
0 → 20
UNI
12
1TCONT,
4 GEM
100.20
VLAN_0
UNI
7
100.15
0 → 15
AT&T Technology Profile

## Slide 16
VLAN_ANY
ANY → ANY
UNI
3
1TCONT,
8 GEM
7.ANY (for UNI 3)
RG
ONU
OLT
(Stag.Ctag)
VLAN_ANY
ANY → ANY
UNI
12
1TCONT,
8 GEM
8.ANY (for UNI 12)
Deutsche Telekom FTTH Technology Profile

## Slide 17
33.ANY
1TCONT, 8 GEM
33.ANY → 540.ANY
DPU with embedded ONU
OLT
(Stag.Ctag)
VLAN_ANY
48.ANY → 600.ANY
CPE
Up to 16
g.fast
48.ANY
1TCONT, 8 GEM
UNI
33.ANY
48.ANY
12
4090
12
4090
1TCONT, 1 GEM
mgmt
33.ANY → 840.ANY
48.ANY → 900.ANY
4090
12
mgmt
33.ANY
1TCONT, 8 GEM
VLAN_ANY
Up to 16
g.fast
48.ANY
1TCONT, 8 GEM
UNI
33.ANY
48.ANY
12
4090
12
4090
1TCONT, 1 GEM
mgmt
Deutsche Telekom FTTB Technology Profile

## Slide 18
HSIA
VoIP
VoD /
IPTV
RG
ONU
OLT
35
HSIA
VoIP
VoD /
IPTV
35
65
55
65
55
35 → 33
65 → 63
65 → 63
55 → 55
35 → 133
65 → 63
55 → 55
7.33
7.34
7.133
HSIA
(Stag.Ctag)
HSIA
VoIP
VoD /
IPTV
35
65
55
UNI
UNI
T-CONTS
35 → 34
55 → 55
1546.63
555.55
VoD
VoIP
IPTV
550
550
550
Turk Telekom Technology Profile

## Slide 19: VOLTHA Architecture
OpenONU
Adaptor
OpenONU
Adaptor
VOLTHA core
Whitebox OLT
OpenOLT
Adaptor
BAL
SDK(s)
OpenOLT driver/agent
ONL
ONIE
ONOS 1
Client
(eg. OFAgent)
Etcd
kafka
OpenONU
Adaptor
OMCI
ONU
ONU
ONU
ONOS 1
ONOS SDN Controller
Applications
VOLTHA: Virtual OLT Hardware Abstraction
Common Control & Management framework shared by all OLTs and ONUs
Hides PON level details (T-CONTS, GEM, OMCI) from the SDN controller by abstracting each PON as a simple Ethernet switch

## Slide 20: SEBA Components: Trellis

## Slide 21
AAA
VOLTHA
SDN Controller - ONOS
Network Edge Mediator (NEM)
SEBA POD
vlans
dhcp
mcast
bridging
routing
ACLs
ONAP
Op X OSS/BSS
Abstract OLT
DockerK8s Helm
OLT
ONU
External BNG
SWITCH
SERVER
SEBA
SDN
Enabled
Broadband
Access
(Embedded BNG)

## Slide 22: Fabric disaggregation → TRELLIS
ONOS: SDN Controller
Trellis Apps Bridging, vRouter, MPLS-SR, mcast, etc.
SCALE
SCALE
External router (BGP, OSPF, etc.)
OpenFlow
P4Runtime
gNMI
In production at Comcast
Carrier-grade SDN fabric for edge/NFV applications
Based on whitebox switches and merchant silicon
Leaf
Leaf
Leaf
Leaf
Spine
Spine
Leaf-Spine Fabric
With ECMP and N-way redundancy
Multi-Stage Leaf-Spine
For distributed access/edge networking
Central office
Field office
Long-haul
Extensive switch support
Vendors: EdgeCore, Delta, Inventec, Stordis, QCT
ASIC: Tomahawk, Tomahawk+, Trident2, Qumran, Tofino
Switch SW stack: ONL, OF-DPA, Stratum
Compute
Compute
Compute
Leaf (ToR)
Single Leaf
metro/ core
Access
OLT
Base station
etc.
Notes: Trellis is a set of SDN apps running on top of ONOS that provide the control plane for a carrier-grade fabric made of whitebox switches running merchant silicon
It can be used to control only 1 switch, like in this example where a top of rack / leaf is used to forward traffic between some access devices, compute servers, and an upstream router. Trellis provide a set of API that let operators enable capabilities such as bridging, routing, multicast, etc. at the network level.
Indeed, the same API and apps can be used to control a full blown leaf-spine fabric, with ECMP and N-way redundancy
...or even a multi-stage fabric where multiple leaf-spines are connected with long-haul optics
What is more, Trellis supports a number of switches from different vendors, running different ASICs and software stacks. Many of these are OCP compliant.
Open APIs such as OpenFlow, P4runtime, and gNMI are used to interact with the devices

## Slide 23
Leaf
Leaf
Spine
Spine
Central Office
Leaf
Leaf
Trellis apps
IPv4/v6 unicast/multicast, vlans, MPLS SR, vRouter …
ONOS Cluster
Internet
Metro/Core
Routers
Base station
R-PHY
R-OLT
Leaf
Leaf
1
Types of Traffic
Optimized for Service Provider Access/Edge
2
Types of Switches

## Slide 24
Leaf
Leaf
Spine
Spine
Central
Office
Leaf
Leaf
Trellis apps
IPv4/v6 unicast/multicast, vlans, MPLS SR, vRouter …
ONOS Cluster
Internet
Metro/Core
Routers
Leaf
Spine
Spine
Leaf
Field Office
Base station
R-PHY
R-OLT
Optimized for Service Provider Access/Edge
3
Distributed
Fabric
Notes: USE CASE 1 – Distributed Fabric for Access/Edge Networking

## Slide 25: Whitebox ToR Switching
BRCM ASIC
BRCM OF-DPA
Indigo OF Agent
OCP Bare Metal Switch
SDK
ONL
ONIE
White-Box =
Open-Hardware Specs (OCP)
+ Open-Source Software (ONF & OCP)
Trellis Apps
SDN Controller
Edgecore
5712, 6712, 7712

## Slide 26: SEBA Components: SD-BNG

## Slide 27: BNG disaggregation → SD-BNG
ONOS: SDN Controller
SDNize
Traditional Chassis-based Vendor Broadband Network Gateway (BNG)
Control Plane Apps (BNG-CP)
Authentication, address assignment, accounting, etc.
User Plane (BNG-UP)
Broadcom Qumran (DNX)
300 Gbit/s, Deep Buffers, HQoS
Intel Barefoot Tofino
3.2 Tbit/s, P4-defined routing, PPPoE term, accounting, etc.
Use merchant silicon available in fabric and OLT
OLT
FABRIC SWITCH
Specialized router:
Subscriber termination (QinQ, PPPoE)
Accounting
Hierarchical QoS
Lawful intercept
Wholesale tunnel relay (L2TP)
Multicast
Routing
Etc.
Notes: The BNG is a specialized type of router that is responsible of routing subscriber traffic to and from the operator core network. It performs many functions, such as…
Similarly to VOLTHA, we disaggregated the BNG black box in two logical pieces: the user plane and the control plane
For the user plane, which is responsible of processing subscriber data traffic, we re-use the same merchant silicon that is already available in the SEBA pod
We can use the Tofino ASIC in the fabric switch to perform functions such as routing, PPPoE termination, accounting, etc
While we can use the Qumran chip inside the OLT to perform Hierarchical QoS, since this chip is specifically designed for application that requires deep buffering
The control plane can run as an SDN apps on top of ONOS

## Slide 28: SEBA 2.0 Architecture
BNG-UP
Core
Docker
Kubernetes
Helm
Network Edge Mediator (NEM)
Edge orchestration and FCAPS micro-services
SEBA POD
ONAP
Operator OSS/BSS
Local adaptor
VOLTHA
Compute
servers
SOFTWARE STACK
HARDWARE
SDN Controller - ONOS
OpenFlow
P4Runtime,
gNMI/OpenConfig
VOLTHA apps PON/OLT control
TRELLIS apps
Fabric control
BNG-CP apps
Subscriber control
Whitebox OLT
Whitebox OLT
whitebox switch
whitebox switch
Stratum
ONU
RG
PON

## Slide 29: SD-BNG with user plane functional split
UPSTREAM
Classification
Double-VLAN termination
PPPoE
term.
Routing
ACL
Accounting
DOWNSTREAM
H-QoS
Double-VLAN aggregation
PPPoE
aggr.
Routing
Classification
ACL
Accounting
Mcast
replication
Anti-spoofing
Policing
Lawful intercept
Lawful intercept
Demonstrated today
Work in progress
Control plane (BNG-c)
User/data plane (BNG-u)
Subscriber addressing
Routing
PPPoE Session Discovery
Authentication
etc.
Barefoot Tofino (fabric sw)
Broadcom Qumran (OLT)

## Slide 30
SEBA SD-BNG Demo at BBWF (Oct 2019)
Webpage
Slides
Subscriber with PPPoE client
ONU
P4 SWITCH
SERVER
OLT

## Slide 31: SEBA Components: NEM

## Slide 32
AAA
VOLTHA
SDN Controller - ONOS
Network Edge Mediator (NEM)
SEBA POD
vlans
dhcp
mcast
bridging
routing
ACLs
ONAP
Op X OSS/BSS
Abstract OLT
DockerK8s Helm
OLT
ONU
External BNG
SWITCH
SERVER
SEBA
SDN
Enabled
Broadband
Access
(Embedded BNG)

## Slide 33: NEM Orchestration & NBI
VOLTHA
ONOS Cluster
vOLT
dhcp
mcast
OF
TP
TP
TP
NNI
OLT
ONU
UNI
Compute
AGG Switch
AGG Switch
SR
FPM
T3
OF
NEM
Redfish
Redfish
SEBA POD
Model based service definition
XOS GUI
XOS Core
Chameleon
Synchronizers
Tosca
Database
OLT,
ONU whitelist,
Subscriber

## Slide 34
SEBA Subscriber Model
Bandwidth Profile
Upstream
Downstream
cir, cbs, eir, ebs, air
cir, cbs, eir, ebs, air
Location
Tagging
OLT/PON port
ONU Serial num
ONU Whitelist
C-tag
S-tag
Service Type
Residential, Business,..
Tech Profile
Num GEM/TCONT
Traffic priorities
Gem-port mappings
Queuing policy
Scheduling policy
Discard policy
Subscriber
SEBA 1.0

## Slide 35: NEM Orchestration & SEBA Workflows
VOLTHA
ONOS Cluster
vOLT
dhcp
mcast
OF
TP
TP
TP
NNI
OLT
ONU
UNI
Compute
AGG Switch
AGG Switch
SR
FPM
T3
OF
NEM
Redfish
Redfish
SEBA POD
BNG is a workflow option
External physical BNG
vBNG in compute
BNG in Agg switches
BNG in OLT boxes
Different operators
==
Different workflows
Authentication is a workflow option
802.1x based
PPPOE based
DHCP based
Subscriber services are workflow options
HSIA
Voice
IPTV
Business services
Technology profiles
Speed profiles
XOS GUI
XOS Core
Chameleon
Synchronizers
Tosca
Database

## Slide 36
NEM Dashboards: XOS GUI
runtime service instantiation, inventory, workflow status

## Slide 37
RG
VOLTHA
ONOS
NNI
OLT
ONU
UNI
Compute
AGG
BNG
NEM
KAFKA
PROMETHEUS
ELK STACK
GRAFANA
KIBANA
XOS
Operator OSS
NEM Monitoring
Infrastructure
Alarms, events & stats
Logs

## Slide 38
NEM Dashboards: Kibana, Grafana
stats, events, logs (FCAPS)

## Slide 39: FCAPS from ONOS
ONOS
vOLT
dhcp
l2relay
igmp
proxy
Bridging/Routing
sadis
AAA
Kafka
integration
Kafka
Prometheus
Grafana

## Slide 40: Redfish API Integration
Kafka
HTTP/REST & REDFISH API
Redfish
Importer
XOS
Edgecore XGS
PON vOLT
Redfish Agent
Edgecore
GPON OLT
Redfish Agent
Edgecore
Switch
Redfish Agent
Server
Redfish Agent
Prometheus
Grafana
NEM

## Slide 41: SEBA 2.0 Architecture
BNG-UP
Core
Docker
Kubernetes
Helm
Network Edge Mediator (NEM)
Edge orchestration and FCAPS micro-services
SEBA POD
ONAP
Operator OSS/BSS
Local adaptor
VOLTHA
Compute
servers
SOFTWARE STACK
HARDWARE
SDN Controller - ONOS
OpenFlow
P4Runtime,
gNMI/OpenConfig
VOLTHA apps PON/OLT control
TRELLIS apps
Fabric control
BNG-CP apps
Subscriber control
Whitebox OLT
Whitebox OLT
whitebox switch
whitebox switch
Stratum
ONU
RG
PON

## Slide 42: SEBA Community

## Slide 43: SEBA (and VOLTHA) Community
AT&T

## Slide 44
Demo setup BBWF 2018
OLTs: Adtran, CIG,
EdgeCore & Iskratel
Servers: VOLTHA, ONOS, XOS, K8s, ELK, Docker, Prometheus, Grafana, Kibana
ONUs: Arcadyan, Alpha, Adtran, CIG, Iskratel
AGG switch: EdgeCore

## Slide 45: SEBA Surge: Brigades
Brigade | Stabilization | BAL 3.0 upgrade | VOLTHA FCAPS | ONOS FCAPS | Multicast & Multi-TCONT | BBSim & Scalability | Test Automation
ONF Mentor | David | Girish | Scott | Saurav | Saurav & Girish | Matteo | Suchitra
Contri-butors |  |  |  |  |  |  | And many others

## Slide 46
SEBA Surge: Brigade Dashboards
SEBA Surge
Started
SEBA Surge
Started
SEBA Surge
Started
SEBA Surge
Started
BBSim & Scalability Brigade
Stabilization Brigade
BAL
Brigade
Multicast Brigade

## Slide 47: SEBA & CORD

## Slide 48
Access Service Orchestration & Control
Mobile vBBU. vMME, vSGW, vPGW, vCDN
ROADM (Core)
BBUs
PON OLTs
Residential vOLT, vSG, vRouter, vCDN
Enterprise vCarrierEthernet, vOAM, vWanEx, vIDS
COTS (Off-the-Shelf) x86 Compute
White-box Switches with
Merchant Silicon
Economies of a datacenter, Agility of a cloud provider
SDN
NFV
Cloud
CORD – Central Office Rearchitected as a Datacenter

## Slide 49: SEBA: Built on CORD
Mobile
ROADM (Core)
Radio Units
PON OLTs
PON OLTs
Residential
Enterprise
Shared Cloud Infrastructure
Residential Services
Mobile Services
Enterprise Services
SEBA
VOLTHA
ODTN
Stratum
ORAN
Trellis
ONOS
NEM Network Edge Mediator OSS mediation & FCAPS support for operationalization Leverages XOS project & toolchain
NEW
SDN
Enabled
Broadband
Access
Notes: SEBA is a platform that brings together a number of ONF projects to virtualize residential access
Today we demonstrate the integration of a new project, Stratum

## Slide 50: SEBA: Built on CORD
Elasticsearch
Logstash
Kibana
Prometheus
Grafana
Network Edge Mediator (NEM)
VOLTHA
SEBA
profile
Hardware: Server, Switch, OLT, ONU etc
AT&T
TT
DT
SEBA POD

## Slide 51: Issues with the previous CORD platform
No distiniction between development vs deployment
  Most of the software built from source at “deploy time”
  Big scripts, scripts calling scripts, long process
  Monolithic: If something breaks, wipe and start from scratch
  Brittle: Small variations of hardware/connectivity could break build
Not flexible or modular
  Required specific versions of server OS
  Tightly coupled components – cannot exclude or replace components
  Required internet access for install
Hard to use
  Choose a profile at start; to change profiles reinstall
  No means for adding services at runtime
Notes: As always, it’s important to translate the input coming from partners’ deployments into requirements, to make the platform better. I’d like to go through some fundamental challenges met with the previous platform, that gave the community some rationale to create the new one. BULLET EXPLAINATION * CORD wasn’t really able to distinguish between a deployment and a development workflow. Most of the time software was built as well during the deployment phases, which is unexpected and time consuming * CORD was spawning VMs during the deployment phase, such requiring either physical machines or VMs * CORD had to be installed on Ubuntu 16.04 * Offline installation was not officially supported, and anyway quite difficult -> problem for most of the SPs * CORD installation was monolithic. It was installing OS, configure OS, install components (i.e. ONOS, OpenStack, XOS) and profiles, together in one step
As a user, you had to decide what “flavor” (use-case) of CORD to install, at the very beginning of the installation. Want to install R-CORD? Choose it at the beginning. Changed your mind and want to install M-CORD? You’ve to reinstall the entire platform
Over time, users (including developers and QA) asked to be able to run CORD in different environments. For example, on single machines for development vs full clusters for trials and production. The two workflows have diverged quite a lot over time and were considerably different from one each other
Many components were tightly coupled, at the point that it was very difficult to exclude them from the system. Classical example: many SPs use their own infra tools (DNS, system configurator like Puppet). CORD providing these services as well, and this was most of the time an issue
Having scripts to automate processes is important, but it’s also important to find the right balance between automation and make difficult for users what’s under the hood
CORD is an integration of effort, using many components. It has been traditionally released as a whole, even if these components have been historically released by different groups. Often it has been a problem to advance features separately

## Slide 52
AAA
VOLTHA
SDN Controller - ONOS
Network Edge Mediator (NEM)
SEBA POD
vlans
dhcp
mcast
bridging
routing
ACLs
ONAP
Op X OSS/BSS
Abstract OLT
DockerK8s Helm
OLT
ONU
External BNG
SWITCH
SERVER
SEBA
SDN
Enabled
Broadband
Access
(Embedded BNG)

## Slide 53
SEBA Modularity
ONU
ONU
OLT
VOLTHA
AGG
switch
Compute
Nodes
ONOS
Access
apps
Fabric
apps
OS
OS
OS
K8s
NEM Orchestration (XOS)
NEM Monitoring
(Prom,Grafana, ELK)
Trellis
Kafka

## Slide 54
Whitebox ToR Fabric Switch
CORD Head Node
CORD Compute Node
ONOS
XOS
Radius
…
VOLTHA
vSG
OvS
EdgeCore 7712 (Tomahawk 32 x 100G)
EdgeCore Whitebox OLT (ASFvOLT16)
Internet
Issues with the previous R-CORD
Residential Subscribers
Central Office
BCM
ONU
RG
CDN
Subscriber Traffic through vSG (virt. Service Gateway)

## Slide 55
AAA
VOLTHA
SDN Controller - ONOS
Network Edge Mediator (NEM)
SEBA POD
vlans
dhcp
mcast
bridging
routing
ACLs
ONAP
Op X OSS/BSS
Abstract OLT
DockerK8s Helm
OLT
ONU
External BNG
SWITCH
SERVER
SEBA
SDN
Enabled
Broadband
Access
(Embedded BNG)

## Slide 56: Summary
ONF: Operator driven curated open source
  CORD is the flagship umbrella project
  SEBA – SDN Enabled Broadband Access, built on the CORD platform
SEBA
  Solution integrates several other ONF projects: VOLTHA, ONOS, Trellis, SD-BNG, XOS
  Current focus areas – VOLTHA productization & SD-BNG exploration
Community
  VOLTHA and SEBA have healthy active communities
  Brigades: a way to effectively manage community resources
  Many brigades in progress, more to come – get involved (CORD Calendar)
Learn More
  Community: https://wiki.opencord.org/display/cord/seba
  Release Documentation: https://guide.opencord.org/cord-7.0/profiles/seba/
  BoM: https://guide.opencord.org/cord-7.0/prereqs/hardware.html